| 3GPP TSG-T2 /ETSI SMG4 |  | T2x00106 |
| --- | --- | --- |
| Vuokatti, Finland, 26-28 September 2000 |  | e.g. for 3GPP use the format TP-99xxx or for SMG, use the format P-99-xxx |
| CHANGE REQUEST | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
|  | 23.057 | CR |  | Current Version: | 3.3.0 |  |
| GSM (AA.BB) or 3G (AA.BBB) specification number ( |  | ( CR number as allocated by MCC support team |
| For submission to: |  | for approval | X |  | strategic |  | (for SMG |
| list expected approval meeting # here ( | for information |  |  | non-strategic |  | use only) |
| Form: CR cover sheet, version 2 for 3GPP and SMG The latest version of this form is available from: ftp://ftp.3gpp.org/Information/CR-Form-v2.doc |
| Proposed change affects: | (U)SIM |  | ME | X | UTRAN / Radio |  | Core Network |  |
| (at least one should be marked with an X) |
| Source: | Motorola | Date: | 26/9/2000 |
| Subject: | Application connection information |
| Work item: | MExE |
| Category: | F Correction |  | Release: | Phase 2 |  |
|  | A Corresponds to a correction in an earlier release |  |  | Release 96 |  |
| (only one category | B Addition of feature |  |  | Release 97 |  |
| shall be marked | C Functional modification of feature | X |  | Release 98 |  |
| with an X) | D Editorial modification |  |  | Release 99 |  |
|  |  |  |  | Release 00 | X |
| Reason for change: | The specification currently states " The user shall be able to obtain information on all connections associated with applications on the MExE MS. ". It is proposed that in order to allow manufacturers to flexibly support the requirement in a more user-friendly way, that the MExE device shall also be able to inform the user of the connections associated MExE with applications. |
| Clauses affected: | 4.9 |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other GSM core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: |  |

<--------- double-click here for help and instructions on how to create a CR.

## 4.9	User control of application connections

This subclause addresses the generic aspects of connection control supported by both WAP and Java classmark MExE MSs.

In order to allow the user to maintain control over connections on his MExE MS and the ability to initiate connections, the user shall be able to terminate or suspend any active connection associated with an application in the MExE environment of the MExE MS. The user shall be able to obtain information about all connections associated with applications on the MExE MS (e.g. requesting information, being informed by the MExE device etc.). Behaviour of the application following termination or suspension of its connection is undefined.

The specific support of connection control by WAP and Java classmark MExE MSs is identified in subsequent subclauses, the security aspects of connection control are identified in the security subclause, and the user control of connection authorisation is identified in the user profile subclause.