3GPP TSG-SA5 (Telecom Management)	S5-023003

Meeting #30 Tampere August 19-23

| 3GPP TSG-T2C UEM JM Tampere, Finland 20-21 August 2002 | T2C-0200034 |
| --- | --- |

| 3GPP TSG-T2 #18 Velen, Germany 12 -16 August 2002 | T2-020698 |
| --- | --- |

Agenda Item:	GUP

Source:	Ericsson

Title:	Comparison of MMS-DataCom parameters in different specifications

Document for:	Discussion

___________________________________________________________________________

1. Introduction

The present document shows how the DataCom parameters relevant for MMS are described in different ways in different specifications.

This highlights the need to have a common identifier and a common description for each of them, independent of the used transport format or specification.

The way to solve this is to apply the DDF concept as described in TS 23.241.

Starting from the MMS parameters, the DataCom parameter names and structures defined in different specifications are listed.

The selected specifications are:

- USIM: the USIM contains MMS configuration parameters. (They can be found under the MMS chapter)

- WAP: the current MMS implementation is based on WAP, and many of the configurable needs are WAP related.

- AT commands 27.007: they provide the mean for a TE to configure the Datacom connections of a MT.

- Core Network protocol 24.008: gives very good information about the values that the different Datacom parameters can have. The information elements included in the messages Call setup for CS and Activate PDP context procedure for PS have been considered.

- QoS 23.107: provides a description of the QoS parameters that a PS connection can take.

In chapter 6 a table shows the relation among the parameters from the different specifications.

2. MMS Configuration parameters in the UE

The following diagram contains the structure of the MMS Configurable parameters as it is in Annex F in TS 23.140. In the USIM specification 31.102, the same parameters are included in Elementary Files.

To see the complete description and possible values of the parameters please refer to TS 23.140.

3. WAP Configuration parameters in the UE

The following diagram contains part of the structure of the WAP Provisioning content as it is described in WAP-183-ProvCont, Provisioning Content. (Not all the possible combination are included, but all the parameter names)

To see the complete description and possible values of the parameters please refer to WAP-183-ProvCont, Provisioning Content.

In the next diagram the PXLOGICAL structure is described in more detail.

4. AT Commands

4.1 PS DataCom Configuration parameters via AT commands in the UE

The following diagram contains the structure of the PDP Context Configuration parameters as they are in described in TS 27.007

To see the complete description and possible values of the parameters please refer to TS 27.007.

4.2 CS DataCom Configuration parameters via AT commands in the UE

The following diagram contains the structure of the Circuit Switch bearer services Configuration parameters, as they are described in TS 27.007

To see the complete description and possible values of the parameters please refer to TS 27.007.

5. Core Network

5.1 Activate PDP context Request Message Information Elements

The following diagram contains the structure of the Information Elements that composes the Activate (secondary) PDP Context Request Message, as they are described in TS 24.008 (Not all the Information Elements are configurable via AT commands or by the user!)

To see the complete description and possible values of the parameters please refer to TS 24.008.

5.2 SETUP Message Information Elements

The following diagram contains the structure of the Information Elements that composed the SETUP Message, as they are described in TS 24.008 (Not all the Information Elements are configurable via AT commands or by the user!)

To see the complete description and possible values of the parameters please refer to TS 24.008.

6. Summary of MMS-DataCom Configuration parameters in the UE

The following table combines all the previous names. It contains the configurable DataCom parameter names given in the MMS, USIM, WAP, AT commands, Core Network protocol and QoS specifications. (To see the complete description and possible values of the parameters please refer to the corresponding specification shown by the column label)

Each row corresponds to a parameter, which is called and described in different ways, depending on which specifications are referenced. For some of them it is obvious that they are the same, but in other cases only by looking at the possible values and descriptions it is possible to recognize that they refer to the same parameter.

This table highlights the need to have a common identifier and a common description for each of them, independent of the used transport format or specification.

|  | MMS 23.140 | USIM 31.102 | WAP Provisioning Content WAP-183-ProvCOnt-20010724-a | AT commands 27.007 | CN protocol 24.008 | QoS 23.107 |
| --- | --- | --- | --- | --- | --- | --- |
|  | MMS Relay/Server address | EFMMSCP (MMS Connectivity Parameters) MMS Relay/server Tag '81' | - | - | - | - |
|  | MMS gateway/proxy |  |  |  |  |  |
|  | Address | EFMMSCP (MMS Connectivity Parameters) MMS Gateway Tag '83' | PXPHYSICAL/PXADDR | - | - | - |
|  | type of address | EFMMSCP (MMS Connectivity Parameters) MMS Gateway Tag '83' | PXPHYSICAL/PXADDRTYPE | - | - | - |
|  | Port | EFMMSCP (MMS Connectivity Parameters) MMS Gateway Tag '83' | PXPHYSICAL/PORTNBR or PXLOGICAL/PORTNBR | - | - | - |
|  | Service | EFMMSCP (MMS Connectivity Parameters) MMS Gateway Tag '83' | PXPHYSICAL/SERVICE or PXLOGICAL/SERVICE | - | - | - |
|  | authentication type | EFMMSCP (MMS Connectivity Parameters) MMS Gateway Tag '83' | PXAUTHINFO/PXAUTH-TYPE | - | - | - |
|  | Authentication id | EFMMSCP (MMS Connectivity Parameters) MMS Gateway Tag '83' | PXAUTHINFO/PXAUTH-ID | - | - | - |
|  | Authentication pw | EFMMSCP (MMS Connectivity Parameters) MMS Gateway Tag '83' | PXAUTHINFO/PXAUTH-PWD | - | - | - |
|  | Core Network Interface |  |  |  |  |  |
|  | Bearer | EFMMSCP (MMS Connectivity Parameters) Interface to Core Network and Bearer Tag '82' | NAPDEF/BEARER | - | - | - |
|  | Address | EFMMSCP (MMS Connectivity Parameters) Interface to Core Network and Bearer Tag '82' | NAPDEF/NAP-ADDRESS | PS: <APN> | PS: Access Point Name CS: Called party BCD number-Number digits | - |
|  | Type of address | EFMMSCP (MMS Connectivity Parameters) Interface to Core Network and Bearer Tag '82' | NAPDEF/NAP-ADDTYPE | - | CS: Called party BCD number-Type of number Called party BCD number-Numbering plan identification | - |
|  | Speed | EFMMSCP (MMS Connectivity Parameters) Interface to Core Network and Bearer Tag '82' | NAPDEF/LINKSPEED NAPDEF/DNLINKSPEED | <speed> | CS: Fixed network user rate | - |
|  | call type | EFMMSCP (MMS Connectivity Parameters) Interface to Core Network and Bearer Tag '82' | NAPDEF/CALLTYPE | <speed> | Modem type Other modem type User rate Rate adaptation Other Rate adaptation | - |
|  | authentication type | EFMMSCP (MMS Connectivity Parameters) Interface to Core Network and Bearer Tag '82' | NAPAUTHINFO/AUTHTYPE | - | protocol identifier? | - |
|  | authentication id | EFMMSCP (MMS Connectivity Parameters) Interface to Core Network and Bearer Tag '82' | NAPAUTHINFO/AUTHNAME | - | - | - |
|  | authentication pw | EFMMSCP (MMS Connectivity Parameters) Interface to Core Network and Bearer Tag '82' | NAPAUTHINFO/AUTHSECRET | - | - | - |
|  | - | - | NAPDEF/LOCAL-ADDR | <PDP_address> | Address information | - |
|  | - | - | NAPDEF/LOCAL-ADDRTYPE | <PDP_type> | PDP type organization PDP type number | - |
|  | - | - | - | <d_comp> | - | - |
|  | - | - | - | <h_comp> | - | - |
|  |  |  |  | TFT |  |  |
|  | - | - | - | <packet filter identifier> | Packet filter identifier | - |
|  | - | - | - | <source address and subnet mask> | packet filter component type identifier packet filter component value | - |
|  | - | - | - | <protocol number (ipv4)/next header (ipv6)> | packet filter component type identifier packet filter component value | - |
|  | - | - | - | <destination port range> | packet filter component type identifier packet filter component value | - |
|  | - | - | - | <source port range> | packet filter component type identifier packet filter component value | - |
|  | - | - | - | <ipsec security paremeter index> | packet filter component type identifier packet filter component value | - |
|  | - | - | - | <Type of service (tos) (ipv4) and mask/traffic class (ipv6) and mask> | packet filter component type identifier packet filter component value | - |
|  | - | - | - | <flow label (ipv6)> | packet filter component type identifier packet filter component value | - |
|  | - | - | - | <evaluation precedence index> | packet filter evaluation precedence | - |
|  |  |  |  | 3G QoS |  |  |
|  | - | - | NAPDEF/DELIVERY-ERR-SDU | <Delivery of erroneous SDUs> | Delivery of erroneous SDUs | Delivery of erroneous SDUs |
|  | - | - | NAPDEF/DELIVERY-ORDER | <Delivery order> | Delivery order | Delivery order |
|  | - | - | NAPDEF/TRAFFIC-CLASS | <Traffic class> | Traffic class | Traffic class |
|  | - | - | NAPDEF/MAX-SDU-SIZE | <Maximum SDU size> | Maximum SDU size | Maximum SDU size |
|  | - | - | MAX-BIT-RATE-UPLINK | <Maximum bitrate UL> | Maximum bit rate for uplink | Maximum bitrate |
|  | - | - | MAX-BIT-RATE-DNLINK | <Maximum bitrate DL> | Maximum bit rate for downlink | Maximum bitrate |
|  | - | - | RESIDUAL-BER | <Residual bit error ratio> | Residual Bit Error Rate | Residual BER |
|  | - | - | SDU-ERROR-RATE | <SDU error ratio> | SDU error ratio | SDU error ratio |
|  | - | - | TRAFFIC-HANDL-PRIO | <Traffic handling priority> | Traffic handling priority | Traffic handling priority |
|  | - | - | TRANSFER-DELAY | <Transfer delay> | Transfer delay | Transfer delay |
|  | - | - | GUARANTEED-BITRATE-UPLINK | <Guaranteed bitrate UL> | Guaranteed bit rate for uplink | Guaranteed bit rate |
|  | - | - | GUARANTEED-BITRATE-DNLINK | <Guaranteed bitrate DL> | Guaranteed bit rate for downlink | Guaranteed bit rate |
|  | - | - | - | - | - | Source statistics descriptor (‘speech’/’unknown’) |
|  |  |  |  | 2G QoS |  |  |
|  | - | - | - | <precedence> | Precedence class | Precedence class |
|  | - | - | - | <delay> | Delay class | Delay class |
|  | - | - | - | <reliability> | Reliablity class | Reliability class |
|  | - | - | - | <peak> | Peak throughput | Peak throughput class |
|  | - | - | - | <mean> | Mean throughput | Mean throughput class |
|  |  |  |  | CS and HSCSD |  |  |
|  | - | - | - | <ce> | Connection element | - |
|  | - | - | - | <name> | Synchronous/asynchronous Transfer mode | - |
|  | - | - | - | <wRx> | Maximum number of traffic channels | - |
|  | - | - | - | <codings> | Acceptable channel codings Acceptable channel codings extended | - |
|  | - | - | - | <wAiur> | Wanted air interface user rate | - |
|  | - | - | - | <topRx> | Maximum number of traffic channels | - |
|  | - | - | - | <mode> | Channel coding Asymmetry Indication | - |
|  | User Preferences/ Notifications |  |  |  |  |  |
|  | - | EFMMSN (MMS Notification) - MMS Implementation | - | - | - | - |
|  | - | EFMMSUP (MMS User Preferences) - MMS User preference profile name Tag '81' | - | - | - | - |
|  | Delivery report | EFMMSUP (MMS User Preferences) MMS User Preference information Tag '82' | - | - | - | - |
|  | Read reply | EFMMSUP (MMS User Preferences) MMS User Preference information Tag '82' | - | - | - | - |
|  | Sender visibility | EFMMSUP (MMS User Preferences) MMS User Preference information Tag '82' | - | - | - | - |
|  | Priority | EFMMSUP (MMS User Preferences) MMS User Preference information Tag '82' |  | - | - | - |
|  | Time of expiry | EFMMSUP (MMS User Preferences) MMS User Preference information Tag '82' | - | - | - | - |
|  | Earliest delivery time | EFMMSUP (MMS User Preferences) MMS User Preference information Tag '82' | - | - | - | - |

7. Conclusions

T2 should agree on a way forward to ensure correct and consistent handling of the MMS-Datacom parameters in the development of all relevant specifications.

The previous table indicates that there is a need to:

- Defining a entry point with unique descriptions for the DataCom parameters, that the other specs (MMS, WAP, AT…) can refer to, in order to keep consistency within the specifications.

- Structuring the DataCom parameters in order to re-use the same parts used by different services/applications. The structure could be like this:

The DDF concept, TS 23.241, was developed with requirement as above in mind, and one way to ensure controlled handling of the MMS-Datacom parameters is to apply the DDF by defining common objects.

The next step is to define the attributes and data types for the parameters listed in the previous table.

8. References

[1]	3GPP TS 24.008 Core Network Protocol

[2]	3GPP TS 23.107 QoS Concept and Architecture

[3]	3GPP TS 23.140: "Multimedia Messaging Service; Stage 2". V5.1.0

[4]	3GPP TS 32.102 USIM

[5]	3GPP 27.007 AT commands

[6]	WAP-183-ProvCont, Provisioning Content