| 3GPP TSG-T2 SWG3 MMS ad hoc Tel Aviv, Israel 11th-13th April, 2000 | T2M00048 |
| --- | --- |

# From:	TSG-T2	 SWG3 MMS adHoc

To:	TSG-S4

Cc:

# Subject:	Media Codec and File Format Selection for MMS

# Contact:	Bernhard Wimmer

Siemens

+49 172 8688920

Bernhard.Wimmer@Mch.Siemens.De

Attachments: 	none

___________________________________________________________________________

The T2 SWG 3 MMS adHoc group is currently defining the Multimedia Messaging Service (MMS) for Release 2000. This includes both the network architecture and the selection of media types, media compression and file formats. For interoperability reasons T2 SWG3 MMS adHoc group intends to find a minimum set of mandatory media type, compression and file formats.

T2 SWG3 MMS adHoc group started discussion on the following media types:

- Image (jpeg, gif, png)

- Video, streaming and non streaming (H.263, MPEG4 visual simple profile level 1, QuickTime)

- Audio, streaming and non streaming (AMR, MP3, MIDI, WAV).

Other media types such as presentation formats, e.g. Mobile SMIL are in discussion.

Due to the expertise of S4 in video and audio coding, T2 SWG 3 MMS adHoc kindly asks S4 to propose a selection of the media compression and file formats. However the media selection may have effects on the network architecture, such as transcoding functionalities or bandwidth/delay requirements for media streaming. Therefore T2 SWG3 MMS adHoc sees a close communication of both groups on this issue.