| 3GPP TSG-T WG2 SWG3#10 Paris, France 21st – 25th January 2002 | T2M020092 |
| --- | --- |
| CR-Form-v5 |
| CHANGE REQUEST |
| ( | 23.140 | CR | CRNum | ( rev | - | ( Current version: | 5.1.0 | ( |
| For HELP on using this form, see bottom of this page or look at the pop-up text over the ( symbols. |
| Proposed change affects: ( | (U)SIM |  | ME/UE | X | Radio Access Network |  | Core Network | X |
| Title: ( | Correction of support for addressing formats on the MM1 interface |
| Source: ( | KPN, Comverse, Openwave Systems |
| Work item code: ( | MESS5-MMS |  | Date: ( | January 17th, 2002 |
| Category: ( | C |  | Release: ( | REL-5 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: 2 (GSM Phase 2) R96 (Release 1996) R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) REL-4 (Release 4) REL-5 (Release 5) |
| Reason for change: ( | Currently the MM1 interface supports E.164 (MSISDN) and/or RFC 822 addressing. This means that operators have the option to implement MMS supporting only one of the two addressing schemes. This leads to interoperability problems between operators with different MM1 addressing schemes. Furthermore MMS UAs, which would only support the E.164 (MSISDN) addressing scheme, would not be able to send MMs to the Internet. These problems could partly be solved in the network, at the expense of considerable costs. So, in order to solve these problems, both addressing schemes should be supported by the MMS UA and the MMS Relay/Server. Also, allow a VASP to be addressed via an alphanumerical alias (“alias”) to facilitate identification of MM1 submissions that are intended for MM7. Finally, some rules for disambiguating untyped addresses are provided. |
| Summary of change: ( | Made both address types mandatory, and added the definition of an “unqualified RFC822 address” Addition of address type in section 7.2.2 |
| Consequences if ( not approved: | Interoperability problems between operators will occur or service costs will increase. There will be no way for MMS Relay/Server to differentiate a MM1 message intended for MM7 delivery. |
| Clauses affected: ( | 7.2.2 |
| Other specs ( |  | Other core specifications ( |  |
| affected: |  | Test specifications |  |
|  |  | O&M Specifications |  |
| Other comments: ( |  |

How to create CRs using this form:

Comprehensive information and tips about how to create CRs can be found at: http://www.3gpp.org/3G_Specs/CRs.htm.  Below is a brief summary:

1)	Fill out the above form. The symbols above marked ( contain pop-up help information about the field that they are closest to.

2)	Obtain the latest version for the release of the specification to which the change is proposed. Use the MS Word "revision marks"  feature (also known as "track changes") when making the changes. All 3GPP specifications can be downloaded from the 3GPP server under ftp://ftp.3gpp.org/specs/ For the latest version, look for the directory name with the latest date e.g. 2001-03 contains the specifications resulting from the March 2001 TSG meetings.

3)	With "track changes" disabled, paste the entire CR form (use CTRL-A to select it) into the specification just in front of the clause containing the first piece of changed text.  Delete those parts of the specification which are not relevant to the change request.

### 7.2.2	Address Formats on MM1

The MMS addressing model on MM1 contains three addresses: the address of the MMS Relay/Server, the address of the recipient and the address of the originator. The address of the MMS Relay/Server shall be the URI of the MMS Relay/Server given by the MMS service provider. Thus, the URI needs to be configurable in the MMS User Agent.

The originator's and the recipient's address could be either a user's address or a user's terminal address. For this release the user's terminal addresses (e.g. terminal IP addresses) are not supported. The MMS User Agent's responsibility is to format these addresses before it submits the message to the originator MMS Relay/Server.

The user’s address can be either an E.164 (MSISDN) or RFC822 address.

The MMS User Agent and MMS Relay/Server shall support both E.164 (MSISDN) and RFC822 addressing formats. When the MMS Relay/Server receives any MM1 sender or recipient address that is an unqualified RFC822 address, the MMS Relay/Server shall form a fully-qualified address using an appropriate domain name before transmitting over MM3 and MM4 reference point interfaces.The reference point MM1 should support a way to indicate the used address type to enable future extension. The encoding of the addressing is up to the corresponding implementation.

E.g. the originator MMS User Agent may specify each of the address fields in one of the following formats:

- RFC 822 address (FQDN or unqualified) ["/TYPE= rfc822"]

- +E.164 ["/TYPE= PLMN"] as [[CC] + NC] + SN

- Other "/TYPE= "

The "/TYPE= " field specifies the address type. When E.164 or RFC822 formats are used the type is optional. The "/TYPE= " convention provides flexibility for future enhancements.

When the “/TYPE=” qualifier is absent, the MMS Relay/Server should resolve potential ambiguities by applying the following logic to the address:

- if it contains the “at-sign” (“@”), the address shall be interpreted as an FQDN ??? RFC822 address

- if it contains an alphanumeric character, it shall be interpreted as an unqualified RFC822 address

- if it is completely numeric, with or without a leading “+”, it shall be interpreted as an E.164 address

- failing the above conditions, the address type would be unknown.

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to http://www.3gpp.org/3G_Specs/3G_Specs.htm

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

Enter a concise description of the subject matter of the CR. It should be no longer than one line.

Enter the source of the CR. This is either (a) one or several companies or, (b) if a (sub)working group has already reviewed and agreed the CR, then list the group as the source.

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, B & C CRs for release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See http://www.3gpp.org/ftp/information/work_plan/

Enter the date on which the CR was last revised.

Enter a single letter corresponding to the most appropriate category listed below. For more detailed help on interpreting these categories, see the Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR was to be rejected. It is necessary to complete this section only if the CR is of category "F" (i.e. correction).

Enter the number of each clause which contains changes.

Enter an X in the box if any other specifications are affected by this change.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.

This is an example of pop-up text.