3GPP TSG- T2 SWG3#10	T2M020106

Paris, France January 21-25 2002

| CR-Form-v4 |
| --- |
| CHANGE REQUEST |
| ( | 23.140 | CR | CRNum | ( rev | - | ( Current version: | 5.1.0 | ( |
| For HELP on using this form, see bottom of this page or look at the pop-up text over the ( symbols. |
| Proposed change affects: ( | (U)SIM |  | ME/UE | X | Radio Access Network |  | Core Network | X |
| Title: ( | MM1 <-> MM4 header mapping |
| Source: ( | Ericsson |
| Work item code: ( | MESS5-MMS |  | Date: ( | 020124 |
| Category: ( | B |  | Release: ( | REL-5 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: 2 (GSM Phase 2) R96 (Release 1996) R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) REL-4 (Release 4) REL-5 (Release 5) |
| Reason for change: ( | For a complete MMS end-to-end solution the information elements used over MM1 needs to be normatively mapped onto the STD 11 headers used over MM4. |
| Summary of change: ( | Addition of annex X, containing mapping tables. |
| Consequences if ( not approved: | No stringent coupling between MM1 and MM4. |
| Clauses affected: ( | new annex X |
| Other specs ( |  | Other core specifications ( |  |
| affected: |  | Test specifications |  |
|  |  | O&M Specifications |  |
| Other comments: ( |  |

How to create CRs using this form:

Comprehensive information and tips about how to create CRs can be found at: http://www.3gpp.org/3G_Specs/CRs.htm.  Below is a brief summary:

1)	Fill out the above form. The symbols above marked ( contain pop-up help information about the field that they are closest to.

2)	Obtain the latest version for the release of the specification to which the change is proposed. Use the MS Word "revision marks"  feature (also known as "track changes") when making the changes. All 3GPP specifications can be downloaded from the 3GPP server under ftp://ftp.3gpp.org/specs/ For the latest version, look for the directory name with the latest date e.g. 2001-03 contains the specifications resulting from the March 2001 TSG meetings.

3)	With "track changes" disabled, paste the entire CR form (use CTRL-A to select it) into the specification just in front of the clause containing the first piece of changed text.  Delete those parts of the specification which are not relevant to the change request.

Annex X (Normative): MM1 <-> MM4 header mappingThis annex maps the information elements found on MM1 onto the STD 11 header fields of MM4.

The tables below are provided to give a normative end-to-end description of MMS. There is a table for each MM1 abstract message with all its information elements in the left column, the right column shows how the MM1 information elements are mapped onto the STD 11 headers of MM4.

In many cases there is no mapping between MM1 information elements and MM4 STD 11 header fields, this is according to specifications. These information elements are included in the tables below in order to give a complete picture of how the MM1 information elements are handled.

Table XX: Mapping MM1_submit.REQ -> MM4_forward.REQ

| Information elements in MM1_submit.REQ | STD11 Header fields in Egress MM4_forward.REQ |
| --- | --- |
| Recipient address | To:, Cc: |
| Content type | Content-Type: |
| Sender address | From: |
| Message class | X-Mms-Message-Class: |
| Date and time | Date: |
| Time of Expiry | X-Mms-Expiry: |
| Earliest Delivery Time | - |
| Delivery report | X-Mms-Delivery-Report: |
| Reply-Charging | - |
| Reply-Deadline | - |
| Reply-Charging-Size | - |
| Priority | X-Mms-Priority: |
| Sender visibility | X-Mms-Sender-Visibility: |
| Read reply | X-Mms-Read-Reply: |
| Subject | Subject: |
| Reply-Charging-ID | - |
| Content | <message body> |

Table XX: Mapping MM1_submit.RES -> MM4_forward.REQ

| Information elements in MM1_submit.RES | STD11 Header fields in Egress MM4_forward.REQ |
| --- | --- |
| Request Status | - |
| Request Status Text | - |
| Message ID | X-Mms-Message-ID: |

Table XX: Mapping MM1_notification.REQ <- MM4_forward.REQ

| Information elements in MM1_notification.REQ | STD11 Header fields in Ingress MM4_forward.REQ |
| --- | --- |
| Message class | X-Mms-Message-Class: |
| Message size | - |
| Time of expiry | X-Mms-Expiry: |
| Message Reference | - |
| Subject | Subject: |
| Priority | X-Mms-Priority: |
| Sender address | From: |
| Delivery report | X-Mms-Delivery-Report: |
| Reply-Charging | - |
| Reply-Deadline | - |
| Reply-Charging-Size | - |
| Reply-Charging-ID | - |
| Element-Descriptor | - |

Table XX: Information elements in the MM1_notification.RES.

| Information elements in MM1_notification.RES | MM4 STD 11 Header fields |
| --- | --- |
| MM Status | - |
| Report allowed | - |

Table XX: Information elements in the MM1_retrieve.REQ

| Information elements in MM1_retrieve.REQ | MM4 STD 11 Header fields |
| --- | --- |
| Message Reference | - |

Table XX: Mapping MM1_submit.REQ <- MM4_forward.REQ

| Information elements in MM1_submit.REQ | STD11 Header fields in Ingress MM4_Forward.REQ |
| --- | --- |
| Message ID | X-Mms-Message-ID: |
| Sender address | From: |
| Content type | Content-type: |
| Recipient address | To: |
| Message class | X-Mms-Message-Class: |
| Date and time | Date: |
| Delivery report | X-Mms-Delivery-Report: |
| Priority | X-Mms-Priority: |
| Read reply | X-Mms-Read-Reply: |
| Subject | Subject: |
| Status | - |
| Status Text | - |
| Reply-Charging | - |
| Reply-Charging-ID | - |
| Reply-Deadline | - |
| Reply-Charging-Size | - |
| Previously-Sent-By | X-Mms-Previously-Sent-By |
| Previously-Sent-Date | X-Mms-Previously-Sent-Date |
| Content | <message body> |

Table XX: Information elements in the MM1_acknowledgement.REQ

| Information elements in MM1_acknowledgement.REQ | MM4 STD 11 Header fields |
| --- | --- |
| Report allowed | - |

Table XX: Mapping MM1_forward.REQ -> MM4_forward.REQ

| Information elements in MM1_forward.REQ | STD11 Header fields in Egress MM4_Forward.REQ |
| --- | --- |
| Recipient address | To:, Cc: |
| Forwarding address | From: |
| Date and time | Date: |
| Time of Expiry | X-Mms-Expiry: |
| Earliest delivery time | - |
| Delivery report | X-Mms-Delivery-Report: |
| Read reply | X-Mms-Read-Reply: |
| Message Reference | - |

Table XX: Information elements in the MM1_forward.RES.

| Information elements in MM1_forward.RES | MM4 STD 11 Header fields |
| --- | --- |
| Status | - |
| Status Text | - |
| Message ID | - |

Table XX: Mapping MM1_delivery_report.REQ <- MM4_delivery_report.REQ

| Information elements in MM1_delivery_report.REQ | STD11 Header fields in Ingress MM4_delivery_report.REQ |
| --- | --- |
| Message ID | X-Mms-Message-ID |
| Recipient address | From: |
| Event Date | Date: |
| MM Status | X-Mms-MM-Status-Code |

Table XX: Mapping MM1_read_reply_recipient.REQ -> MM4_read_reply_report.REQ

| Information elements in MM1_read_reply_recipient.REQ | STD11 Header fields in Egress MM4_read_reply_report.REQ |
| --- | --- |
| Recipient address | From: |
| Originator address | To: |
| Message-ID | X-Mms-Message-ID: |
| Date and Time | Date: |
| Read Status | X-Mms-Read-Status: |

Table XX: Mapping MM1_ read_reply_originator.REQ <- MM4_ read_reply_report.REQ

| Information elements in MM1_read_reply_originator.REQ | Ingress STD11 Header fields in MM4_read_reply_report.REQ |
| --- | --- |
| Recipient address | From: |
| Originator address | To: |
| Message-ID | X-Mms-Message-ID: |
| Date and Time | Date: |
| Read Status | X-Mms-Read-Status: |

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to http://www.3gpp.org/3G_Specs/3G_Specs.htm

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

Enter a concise description of the subject matter of the CR. It should be no longer than one line.

Enter the source of the CR. This is either (a) one or several companies or, (b) if a (sub)working group has already reviewed and agreed the CR, then list the group as the source.

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, B & C CRs for release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See http://www.3gpp.org/ftp/information/work_plan/

Enter the date on which the CR was last revised.

Enter a single letter corresponding to the most appropriate category listed below. For more detailed help on interpreting these categories, see the Technical Report 21.900 "3GPP working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR was to be rejected. It is necessary to complete this section only if the CR is of category "F" (i.e. essential correction).

Enter each the number of each clause which contains changes.

Enter an X in the box if any other specifications are affected by this change.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.

This is an example of pop-up text.