ETSI SMG4	TSGT2#2(99)287

London, 15-19 March 1999

| CHANGE REQUEST No : |
| --- |
| Technical Specification GSM | 07.07 | Version: | 7.2.0 |
|  | Submitted to SMG | 29 | for approval | x | without presentation ("non-strategic") | X |
|  | list SMG plenary meeting no. here ­ | for information |
| with presentation ("strategic") |

| Proposed change affects: | SIM |
| --- | --- |
| ME | X | Network |

(at least one should be marked with an X)

| Work item: | TEI |
| --- | --- |

| Source: | Ericsson | Date: | 990312 |
| --- | --- | --- | --- |

| Subject: | New command for setting of Date format |
| --- | --- |

| Category: | F Correction |
| --- | --- |
| Release: | Phase 2 |
| A Corresponds to a correction in an earlier release |
|  | Release 96 |
|  | (one category | B Addition of feature | X |
| Release 97 |
|  | and one release | C Functional modification of feature |
|  | Release 98 |
|  | only shall be | D Editorial modification |
|  | Release 99 | X |
| marked with an X) |

Reason for change:

Added functionality for setting of date format for the date information presented on the ME’s display.

| Clauses affected: | 6.xx |
| --- | --- |

| Other specs | Other releases of same spec |
| --- | --- |
| ® List of CRs: |
|  | affected: | Other core specifications |
| ® List of CRs: |
| MS test specifications / TBRs |
| ® List of CRs: |
| BSS test specifications |
| ® List of CRs: |
| O&M specifications |
| ® List of CRs: |

Other comments:

6.19	Settings date format +CSDF

Table 1: +CSDF parameter command syntax

| Command | Possible response(s) |
| --- | --- |
| +CSDF=[<mode>] | +CME ERROR: <err> |
| +CSDF? |

+CSDF:<mode>

+CME ERROR: <err>

+CSDF=?

+CSDF:(list of supported <mode>s)

+CME ERROR: <err>

Description

This command sets the date format of the date information presented to the user.

Defined values

<mode>:  NOTE: It is manufacturer specific which modes that are supported.

DD-MMM-YYYY		NOTE: Presentation of MMM is language dependent.

DD-MM-YY

MM/DD/YY

DD/MM/YY

DD.MM.YY

YYMMDD

YY-MM-DD

8-255     Manufacturer specific

Implementation

Optional