SMG4/TSG-CN3/TSG-T2

| London, UK, 15-19 March 1999 | TSGT2#2(99)102 |
| --- | --- |

ETSI SMG9 Ad Hoc 	Tdoc 9z99-008

Newbury, 10 – 12 March 1999

Liaison Statement

From:	SMG9 Secure Messaging Ad Hoc

To:	SMG4

CC:	SMG9

Subject:	Modifying the use of reserved CB data Download MID values

SMG9 have identified the need to secure SMS-CB Data Download messages.  To this end, an Ad Hoc meeting has started work on modifying GSM 03.48 to define the structure for this.

The Ad Hoc investigated GSM 03.41, and have noted that a range of Message Identifiers (MID) are reserved for CB Data Download, specifically 1000 to 10FF (hex).

The Ad Hoc propose splitting the already reserved range in half, so that half the MID range is used to indicate CB Data Download messages sent in "clear", and the other half identify the CB contents being secured according to GSM 03.48.

The Ad Hoc have drafted a proposed Change Request to GSM 03.41 to reflect this proposal, and request SMG4 to approve it after appropriate deliberation.  This proposed Change Request is contained in Tdoc 9z99-009.

ATTACHED: Tdoc 9z99-009 (proposed CR to GSM 03.41)

ETSI SMG9 Ad Hoc 	Tdoc  9z99-009

Newbury, 10 – 12 March 1999

| CHANGE REQUEST No : |
| --- |
| Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
| Technical Specification GSM | 03.41 | Version: | 7.0.0 |
|  | Submitted to SMG |
| for approval |
| without presentation ("non-strategic") |
| list SMG plenary meeting no. here ( | for information |
| with presentation ("strategic") |
| PT SMG CR cover form is available from: http://docbox.etsi.org/tech-org/smg/Document/smg/tools/CR_form/crf28_1.zip |

| Proposed change affects: | SIM | X | ME |
| --- | --- | --- | --- |
| Network | X |

(at least one should be marked with an X)

| Work item: | TEI |
| --- | --- |

| Source: | SMG9 Secure messaging Ad Hoc | Date: | March 1999 |
| --- | --- | --- | --- |

| Subject: | Allowing SMS-CB secure Data Download |
| --- | --- |

| Category: | F Correction |
| --- | --- |
| Release: | Phase 2 |
| A Corresponds to a correction in an earlier release |
|  | Release 96 |
|  | (one category | B Addition of feature |
|  | Release 97 |
|  | and one release | C Functional modification of feature | X |
| Release 98 |
|  | only shall be | D Editorial modification |
|  | Release 99 | X |
| marked with an X) |

Reason for change:

There is a need to secure SIM Data Download using SMS-CB; this Change Request re-assigns part of the already assigned MID range for SIM Data Download specifically for secure messaging for SIM Data Download.

| Clauses affected: | 1.1 and 9.3.2.2 |
| --- | --- |

| Other specs | Other releases of same spec |
| --- | --- |
| ( List of CRs: |
|  | affected: | Other core specifications |
| ( List of CRs: |
| MS test specifications / TBRs |
| ( List of CRs: |
| BSS test specifications |
| ( List of CRs: |
| O&M specifications |
| ( List of CRs: |

Other comments:

1	Scope

This Technical Specification describes the Cell Broadcast short message service (CBS). It defines the primitives over the Cell Broadcast Centre - Base Station System (CBC-BSS) interface and the message formats over the Base Station System - Mobile Station (BSS-MS) interface for Teleservice 23 as specified in GSM 02.03 [2].

1.1	Normative references

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

For a specific reference, subsequent revisions do not apply.

For a non-specific reference, the latest version applies.

A non-specific reference to an ETS shall also be taken to refer to later versions published as an EN with the same number.

………….

[8]	GSM 05.02: "Digital cellular telecommunication system (Phase 2+); Multiplexing and multiple access on the radio path".

[9]	GSM 07.05: "Digital cellular telecommunication system (Phase 2+); Use of Data Terminal Equipment - Data Circuit terminating Equipment (DTE - DCE) interface for Short Message Service (SMS) and Cell Broadcast Service (CBS)".

[10]	GSM 08.52: "Digital cellular telecommunication system (Phase 2+); Base Station Controller - Base Transceiver Station (BSC - BTS) interface  Interface principles".

[11]	GSM 08.58: "Digital cellular telecommunication system (Phase 2+); Base Station Controller - Base Transceiver Station (BSC - BTS) interface  Layer 3 specification".

[12]	CCITT Recommendation X.210: "Open systems interconnection layer service definition conventions".

[13]	GSM 08.08 MSC-BSS Interface Layer 3 specification

[14]	GSM 03.42: “ Compression algorithm for text messaging services”.

[15]	GSM 03.48: "Digital cellular telecommunications system (Phase 2+); Security Mechanisms for the SIM application toolkit; Stage 2"

9.3.2.2	Message Identifier

This parameter identifies the source and type of the message. For example, "Automotive Association" (= source), " Traffic Reports" (= type) could correspond to one value. A number of messages may originate from the same source and/or be of the same type. These will be distinguished by the Serial Number. The Message Identifier is coded in binary.

The ME shall attempt to receive the CBS messages whose Message Identifiers are in the "search list". This "search list" shall contain the Message Identifiers stored in the EFCBMI, EFCBMID and EFCBMIR files on the SIM (see GSM 11.11) and any Message Identifiers stored in the ME in a "list of CBS messages to be received". If the ME has restricted capabilities with respect to the number of Message Identifiers it can search for, the Message Identifiers stored in the SIM shall take priority over any stored in the ME.

The use/application of the Message Identifier is shown in the following list, with octet 3 of the Message Identifier shown first, followed by octet 4. Thus "1234" (hex) represents octet 3 = 0001 0010 and octet 4 = 0011 0100.

0000 - 03E7 (hex):	To be allocated by PLMN operator associations. If a Message Identifier from this range is in the "search list", the ME shall attempt to receive such message.

This version of GSM 03.41 does not prohibit networks from using Message Identifiers in the range 0000 - 03E7 (hex) for Cell Broadcast Data Download to the SIM.

03E8 - 0FFF (hex):	Intended for standardization in future versions of GSM 03.41. These values shall not be transmitted by networks that are compliant to this version of GSM 03.41. If a Message Identifier from this range is in the "search list", the ME shall attempt to receive this message.

1000 - 10FF 107F (hex):	Networks shall only use Message Identifiers from this range for Cell Broadcast Data Download in "clear" to the SIM (see GSM 11.14). If a message Identifier from this range is in the "search list", the ME shall attempt to receive this message.

1080 – 10FF (hex):	Networks shall only use Message Identifiers from this range for Cell Broadcast Data Download secured according to GSM 03.48 [15] to the SIM (see GSM 11.14). If a message Identifier from this range is in the "search list", the ME shall attempt to receive this message.

1100 - 9FFF (hex):	intended for standardization in future versions of GSM 03.41. These values shall not be transmitted by networks that are compliant to this version of GSM 03.41. If a Message