| SMG4/TSG-CN3/TSG-T2 London, UK, 15-19 March 1999 | TSGT2#2(99)210 |
| --- | --- |

| CHANGE REQUEST No : |  | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
| --- | --- | --- |
| Technical Specification GSM / UMTS: | 03.57 | Version | 1.5.0 |  |
| Submitted to SMG |  | For approval |  | without presentation ("non-strategic") |  |  |
| list plenary meeting or STC here ( | for information |  | with presentation ("strategic") |  |  |
| PT SMG CR cover form. Filename: crf26_3.doc |

| Proposed change affects: | SIM |  | ME | X | Network |  |
| --- | --- | --- | --- | --- | --- | --- |

(at least one should be marked with an X)

| Work item: | MExE |
| --- | --- |

| Source: | Motorola | Date: | xx/02/99 |
| --- | --- | --- | --- |

| Subject: | User Interface table improvement |
| --- | --- |

| Category: | F Correction |  | Release: | Phase 2 |  |
| --- | --- | --- | --- | --- | --- |
|  | A Corresponds to a correction in an earlier release |  |  | Release 96 |  |
| (one category | B Addition of feature |  |  | Release 97 |  |
| and one release | C Functional modification of feature | X |  | Release 98 | X |
| only shall be | D Editorial modification |  |  | Release 99 |  |
| marked with an X) |  |  |  | UMTS |  |

| Reason for change: | The user interface table is ambiguous in terms of:- level of user preferences preferences which may be recorded coding of the tokens This changes proposes that:- some preferences are removed (i.e. background, font-colour, font-size, softkey, input mode etc.), existing ones are replaced with more specific ones (i.e. supplementary-services is replaced with call-waiting, call-barring and call-diverting) the preferred network selection is added |
| --- | --- |

| Clauses affected: | 4.6.2 |
| --- | --- |

| Other specs | Other releases of same spec |  | ( List of CRs: |  |
| --- | --- | --- | --- | --- |
| affected: | Other core specifications |  | ( List of CRs: |  |
|  | MS test specifications / TBRs |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |

| Other comments: |  |
| --- | --- |

### 4.6.2	User interface customisation tokens

To support the user customisation of the interface, and portability of the preferences, table 2 defines the customisation tokens.

|  |  |  |  |  | Security Level |
| --- | --- | --- | --- | --- | --- |
| Token | User Interface Customisation | 1 | 2 | 3 | 4 |
| Logo | Modify service provider logo | O | - | - | - |
| Custom-services | Enable/disable network operator custom services | O | - | - | - |
| Network-Selection | Network selection procedure | O? | - | O | - |
| Icon | Add/modify icon | - | - | O | - |
| Menu-modify | Add/remove menu item | - | - | O | - |
| Menu-activation | Enable/disable menu item | - | - | O | - |
| Phonebook | Add/modify SIM or ME phonebook entry | - | - | O | - |
| Language | Preferred language | - | - | O | - |
| Call-Diversion | Modify call diversion | - | - | O | - |
| Call-Barring | Modify call barring | - | - | O | - |
| Call-Waiting | Modify call waiting | - | - | O | - |
| Voicemail | Add/modify voicemail number | - | - | O | - |
| Ringer-Mode | Modify phone ringer mode | - | - | O | - |
| Extended-menus | Enable/Disable extended menus | - | - | O | - |
| Add-char | Additional characteristics | - | - | O | - |
| Add-info | Additional Information | - | - | O | - |

Table 2: User interface customisation