| 3GPP TSG-T2#4 / ETSI SMG4 Miami, US, 14-16 June 1999 | TSGT2#4(99)479 |
| --- | --- |

ETSI STC SMG1 meeting # 64 (99/2)		SMG1 (99)173

Quebec City 5th - 6th July 1999	Agenda Item:

ETSI SMG1 SIM Tool Kit Ad-hoc               	Tdoc SMG1 Ad-hoc 032/99

Bonn, Germany, May, 1999

# Liaison

# From: SMG1/9 SAT ad hoc

To: SMG1, S1, SMG1 CAMEL, SMG4 MExE, T2 MExE, SMG3, SMG3 WPC CAMEL

CC: SMG9, SMG10

Subject: SAT/MExE  <-> CAMEL Interworking / Traceability

Proposed for: Decision, Action

SMG1/9 SAT ad hoc meeting has discussed the interworking between SAT/MExE and CAMEL and traceability of SAT/MExE actions and came to following conclusion:

SMG1 SAT ad hoc proposed to introduce an information field in the call set up messages between the ME and the MSC that can be used by SAT or MExE applications for application identification and be extended by a free formatted field for interworking purposes.

This information element could be included in the call records to cover the SAT/MExE traceability requirements and should be included in the IPD message towards the CAMEL CSE for interworking purposes.

For MT calls the CAMEL CSE should be capable of filling this field also for interworking purposes and a SAT or MExE application can analyse the information in the ME for further action.

SMG1/9 Ad hoc has included the requirement in the current SAT stage 1 for Release ‘99.

Service Example:

To implement an MSP feature based on SAT/MExE and CAMEL an application can include inside the call setup message an identification if the current call is e.g. a private or a business call. This information can be analysed in the call records and/or a CAMEL environment to derive the correct account and include the corresponding calling party number in the call set up message.

In case of a mobile terminated call, a CSE may include information if the incoming call is a business or private one.  An MS based application can analyse this information and initiate a corresponding indication towards the user.

Proposed Actions:

- SMG1/3 CAMEL is asked to support this topic and to include it in the current stage 1 for CAMEL phase 3.

- SMG1/4 MExE is asked to check if this feature is useful for MExE purposes and to include the requirement in the current stage 1 if applicable.

- On positive decision of SMG 1, SMG3 and SMG3 WPC CAMEL are asked to define the information field and to include it in the corresponding messages between ME and MSC and gsmSSF and CSE, if possible for Release 99.