| 3GPP TSG-T2#4 / ETSI SMG4 Miami, US, 14-16 June 1999 | TSGT2#4(99)xxx |
| --- | --- |

Technical Specification Group, Radio Access Network	TSGR#4(99)319

Meeting #4, Miami, 17-18 June 1999

Source:	Editor

Title:	TR 25.925 « Radio Interface for Broadcast/Multicast Services »,
Version 0.1.0

Document for:	For information

Agenda Item:	6.2

TR 25.925 V0.1.0 (1999-06)

Technical Report

3rd Generation Partnership Project (3GPP);

Technical Specification Group (TSG) RAN;

Working Group 2 (WG2);

Radio Interface for Broadcast/Multicast Services

The present document has been developed within the 3rd Generation Partnership Project (3GPP TM) and may be further elaborated for the purposes of 3GPP. The present document has not been subject to any approval process by the 3GPP Organisational Partners and shall not be implemented. This Specification is provided for future development work within 3GPP only. The Organisational Partners accept no liability for any use of this Specification. Specifications and reports for implementation of the 3GPP TM system should be obtained via the 3GPP Organisational Partners' Publications Offices.

Reference

<Workitem> (<Shortfilename>.PDF)

Keywords

Digital cellular telecommunications system, Universal Mobile Telecommunication System (UMTS), UTRA, IMT-2000

3GPP

Postal address

Office address

Internet

secretariat@3gpp.org

Individual copies of this  deliverable
can be downloaded from

http://www.3gpp.org

Copyright Notification

No part may be reproduced except as authorized by written permission.
The copyright and the foregoing restriction extend to reproduction in all media.

©

All rights reserved.

Contents

1	Scope	5

2	References	5

3	Definitions and Abbreviations	6

3.1	Definitions	6

3.2	Abbreviations	6

4	Overview of Point-to-multipoint Services and Requirements	7

5	Common Model	11

6	SMS Cell Broadcast Service (GSM)	11

6.1	Radio Interface Requirements	11

6.2	Impact on UTRAN functions	11

7	PTM-Multicast Service (GPRS)	11

7.1	Radio Interface Requirements	11

7.2	Impact on UTRAN Functions	11

8	PTM-Group Call Service (GPRS)	12

8.1	Radio Interface Requirements	12

8.2	Impact on UTRAN Functions	12

9	IP Multicast Service (GPRS)	12

9.1	Radio Interface Requirements	12

9.2	Impact on UTRAN Functions	12

10	Multimedia Distribution Service (UMTS)	12

10.1	Radio Interface Requirements	12

10.2	Impact on UTRAN Functions	12

Annex A: Functions related to MDS (ffs.)	13

Intellectual Property Rights

IPRs essential or potentially essential to the present deliverable may have been declared to 3GPP and/or its organizational partners. The information pertaining to these essential IPRs, if any, is publicly available for 3GPP members and non-members, free of charge. This can be found in the latest version of the 3GPP Technical Report:

[reference tbd.]

Pursuant to the 3GPP Interim IPR Policy, no investigation, including IPR searches, has been carried out by 3GPP. No guarantee can be given as to the existence of other IPRs not referenced in the [tbd.], which are, or may be, or may become, essential to the present document.

Foreword

This Technical Report has been produced by the 3GPP.

The contents of the present document are subject to continuing work within the TSG and may change following formal TSG approval. Should the TSG modify the contents of this TR, it will be re-released by the TSG with an identifying change of release date and an increase in version number as follows:

Version x.y.z

where:

x	the first digit:

1	presented to TSG for information;

2	presented to TSG for approval;

3	Indicates TSG approved document under change control.

y	the second digit is incremented for all changes of substance, i.e. technical enhancements, corrections, updates, etc.

z	the third digit is incremented when editorial only changes have been incorporated in the specification;

# Scope

The present document shall provide a general overview on radio interface related aspects of broadcast/multicast services. Also in the scope of this report is the functional split between UTRAN nodes and the analysis of the potential impact on UTRAN related interfaces regarding broadcast/multicast services. This report covers stage 2 and stage 3 aspects.

This report is organized as follows: Chapter 4 gives an overview on the broadcast/multicast services and their requirements. Chapter 5 provides a common model and describes aspects common to all point-to-multipoint services. Chapters 6 - 10 are devoted to the different broadcast/multicast service categories. Each service specific chapter describes the requirements on the interfaces. In these subchapters the impacts on the interface functions and the protocol aspects are described. This TR covers only those items which are in the scope of 3GPP TSG RAN. Information from Technical Specifications or other documents are provided when it is necessary to understand the requirements described.

Table 1: Schedule of the broadcast/multicast services onto the UMTS phases and annual releases

| Phase | (Annual) Release | Broadcast/multicast serviee |
| --- | --- | --- |
| 1 | 1999 | SMS Cell Broadcast Service (GSM) |
|  | 2000 |  |
|  | 2001 |  |

Note: A decision to map the services to phases/releases is required for all other broadcast/multicast services.

# References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

- References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

- For a specific reference, subsequent revisions do not apply.

- For a non-specific reference, the latest version applies.

- A non-specific reference to a TS shall also be taken to refer to later versions published as an EN with the same number.

[1]	3GPP TS 22.100 “ UMTS Phase 1”

[2]	3GPP TS 22.101 “ UMTS Serive Principle”

[3]	3GPP TS 22.105 “Services and Service Capabilities”

[4]	3GPP TS 25.301 "Radio Interface Protocol Architecture"

[5]	3GPP TS 25.302 "Services provided by the Physical Layer"

[6]	3GPP TS 25.303 "UE Funtions and Interlayer Procedures in Conneted Mode"

[7]	3GPP TS 25.304 "UE Procedures in Idle Mode"

[8]	3GPP TS 25.321 "MAC Protolcol Specification

[9]	3GPP TS 25.322 "RLC Protolcol Specification

[8]	3GPP TS 25.331 "RRC Protolcol Specification

[9]	GSM 02.03: "Digital cellular telecommunications system (Phase 2+); Principles of telecommunication services supported by a GSM Public Land Mobile Network (PLMN)".

[10]	GSM 02.60: "GPRS Service description"

[11]	GSM 03.41: "Digital cellular telecommunications system (Phase 2+); Man-Machine Interface (MMI) of the Mobile Station (MS)"

[12]	GSM 03.61: "Digital cellular telecommunications system (Phase 2+); Support of Mobile Number Portability (MNP); Service description; Stage 1"

# Definitions and Abbreviations

## Definitions

## Abbreviations

CB	Cell Broadcast

IP	Internet Protocol

IP-M	IP Multicast

MDS	Multimedia Distribution Service

PTM	Point-to-Multipoint

PTM-G	PTM Group Call

PTM-M	PTM Multicast

SMS	Short Message Service

SMS-CB	SMS Cell Broadcast

UE	User Equipment

UMTS	Universal Mobile Telecommunication System

UTRAN	UMTS Terrestrial Radio Access Network

# Overview of Point-to-multipoint Services and Requirements

It is agreed to have service continuity for GSM/GPRS point-to-multipoint services in UMTS ([1] and [2]). This means that the user gets the same service behaviour as he knows it form GSM or GPRS. The services are SMS Cell Broadcast [101] and Point-to-multipoint Multicast, Point-to-multipoint Group Call and IP Multicast [102].

Combined with the UMTS service classification given in [2] the service classification shown in Figure 1 could be used as a starting point. The figure contains the view in terms of Radio Access Bearer services and should not be applied for higher layers where other categories of services may exist. Future work may result in changes of Figure 1.

Figure 1: Structure of point-to-multipoint services

Tables 1 and 2 below summarize the service attributes defining the broadcast/multicast services.  Table 3 allocates attributes of the Uu radio interface to the services. Table entries which are left empty, require further study.

Table 1: Bearer Service attributes  ([3])

| Attributes |  | Values |
| --- | --- | --- |
| Information transfer attributes | 1. Connection mode attribute | Connection oriented: CO (Circuit Switched base) |
|  |  | Connectionless: CL (Packet Switched) |
|  | 2. Transfer type attribute | Constant bit rate |
|  |  | Variable bit rate |
|  |  | Available bit rate |
|  |  | Unspecified bit rate |
|  | 3. Symmetry attribute | Unidirectional |
|  |  | Bi-directional symmetric |
|  |  | Bi-directional asymmetric |
|  | 4. Communication configuration attribute | Point-to-point |
|  |  | Point-to-multipoint |
|  | 5. Information transfer rate attributes | (Continuous rage of values is possible) |
|  |  | High bit rate |
|  |  | Medium bit rate |
|  |  | Low bit rate |
| Information quality attributes | 1. Maximum transfer delay attribute | (Continuous rage of values is possible) |
|  |  | Delay sensitive |
|  |  | Delay insensitive |
|  | 2. Delay variation attribute | (Continuous rage of values is possible) |
|  |  | Constant |
|  |  | Variable |
|  | 3. Bit error ratio attribute | (Continuous rage of values is possible) |
|  |  | Loss sensitive |
|  |  | Loss insensitive |
|  | 4. Error characteristics attribute | Uniform |
|  |  | Bursty |

Table 2: Overview of Broadcast/Multicast Services (Part 1)

| Attributes | SMS-CB | PTM Multicast (medium rate) | PTM Multicast (high rate) | PTM Group call | IP-multicast (Medium rate) | IP-multicast (Low rate) |
| --- | --- | --- | --- | --- | --- | --- |
| Information transfer attributes |  |  |  |  |  |  |
| 1. Connection mode attribute | CL | CL | CL | CO | CL | CL |
| 2. Transfer type attribute | Constant | Variable | Variable | Variable | Available | Available |
| 3. Symmetry attribute | UNI | UNI | UNI | UNI BI ASYM MULTI | MULTI (UNI) | MULTI (UNI) |
| 4. Communication configuration attribute | PTM | PTM | PTM | PTM | PTM | PTM |
| 5. Information transfer rate attributes | Low | Medium | High | Low | Medium | Low |
| Information quality attributes |  |  |  |  |  |  |
| 1. Maximum transfer delay attribute | Delay insensitive | Delay insensitive | Delay sensitive | Delay sensitive | Delay insensitive | Delay insensitive |
| 2. Delay variation attribute |  |  |  |  |  |  |
| 3. Bit error ratio attribute | Loss insensitive | Loss insensitive | Loss insensitive | Loss insensitive | Loss sensitive | Loss sensitive |
| 4. Error characteristics attribute |  |  |  |  |  |  |
| Defined in | GSM | GPRS | GPRS | GPRS | GPRS | GPRS |

(Editor’s note: Value MULTI is not defined in [3] yet. It is specified in [10])

Table 2: Overview of Broadcast/Multicast Services (Part 2)

| Attributes | MDS without user control (high rate) | MDS without user control (medium rate) | MDS with user control (high rate) | MDS with user control (medium rate) | Messaging service (high rate) | Messaging service (medium rate) |
| --- | --- | --- | --- | --- | --- | --- |
| Information transfer attributes |  |  |  |  |  |  |
| 1. Connection mode attribute |  |  |  |  |  |  |
| 2. Transfer type attribute |  |  |  |  |  |  |
| 3. Symmetry attribute |  |  |  |  |  |  |
| 4. Communication configuration attribute | PTM | PTM | PTM | PTM | PTM | PTM |
| 5. Information transfer rate attributes | High | Medium | High | Medium | High | Medium |
| Information quality attributes |  |  |  |  |  |  |
| 1. Maximum transfer delay attribute |  |  |  |  |  |  |
| 2. Delay variation attribute |  |  |  |  |  |  |
| 3. Bit error ratio attribute |  |  |  |  |  |  |
| 4. Error characteristics attribute |  |  |  |  |  |  |
| Defined in | UMTS | UMTS | UMTS | UMTS | UMTS | UMTS |

Table 3: Radio Interface related attributes of broadcast/multicast services (part 1)  [10]

| Attributes | SMS-CB | PTM Multicast (medium rate) | PTM Multicast (high rate) | PTM Group call | IP-multicast (Medium rate) | IP-multicast (Low rate) |
| --- | --- | --- | --- | --- | --- | --- |
| UE modes (ffs.) | (ffs.) |  |  |  |  |  |
| Logical Channels | CTCH | CTCH | CTCH | CTCH | CTCH | CTCH |
| Necessity of separate control channel | No |  |  |  |  |  |
| Transport Channels | FACH |  |  |  |  |  |
| Physical Channels | Secondary CCPCH |  |  |  |  |  |
| DRX Mode | Yes | Yes | Yes | No | Yes | Yes |
| Primary addressing | GEO area | Subsciber group | Subscriber group | Subscriber group | Subscriber group | Subscriber group |
| Secondary addressing | --- | GEO area | GEO area | GEO area | --- | --- |
| Present subscribers known | No | No | No | Yes | Yes | Yes |
| Ciphering | No | No | No | Yes | Yes | Yes |
| Reliable delivery | No | No | No | Optional | Yes | Yes |

Table 3: Radio Interface related attributes of broadcast/multicast services (part 2)

| Attributes | MDS without user control (high rate) | MDS without user control (medium rate) | MDS with user control (high rate) | MDS with user control (medium rate) | Messaging service (high rate) | Messaging service (medium rate) |
| --- | --- | --- | --- | --- | --- | --- |
| UE modes (ffs.) |  |  |  |  |  |  |
| Logical Channels |  |  |  |  |  |  |
| Necessity of separate control channel |  |  |  |  |  |  |
| Transport Channels |  |  |  |  |  |  |
| Physical Channels |  |  |  |  |  |  |
| DRX Mode |  |  |  |  |  |  |
| Primary addressing |  |  |  |  |  |  |
| Secondary addressing |  |  |  |  |  |  |
| Present subscribers known |  |  |  |  |  |  |
| Ciphering |  |  |  |  |  |  |
| Reliable delivery |  |  |  |  |  |  |

# Common Model

The common Traffic Channel (CTCH) [4] is provided by the MAC sublayer for support of broadcast/multicast services. It is presently assumed that the CTCH can be used for all categories of broadcast/multicast services.

The present assumption (ffs.) for SMS-CB service is that the CTCH is mapped to a FACH transport channel. The FACH is also a candidate to be used for other multicast services. This possibility will be further investigated in this report.

# SMS Cell Broadcast Service (GSM)

Functions which are not under scope of RAN are:

- Mapping of geographical area onto cells

Functions which are under scope of RAN are:

- Scheduling of SMS CB messages per cell

- Usage of transparent or unacknowledged (L2) services

## Radio Interface Requirements

## Impact on UTRAN functions

# PTM-Multicast Service (GPRS)

This chapter contains the requirements derived from GPRS specifications of Point-to-multipoint Multicast service and the analysis regarding the UMTS radio interface Uu.

Note: 
The specification of the PTM-Multicast service is part of the work item “GPRS – Point-To-Multipoint Services” of GSM Phase 2+ Release 1999.

## Radio Interface Requirements

## Impact on UTRAN Functions

# PTM-Group Call Service (GPRS)

This chapter contains the requirements derived from GPRS specifications of Point-to-multipoint Group Call service and the analysis regarding the UMTS radio interface Uu.

Note: 
The specification of the PTM-Group Call service is part of the work item “GPRS – Point-To-Multipoint Services” of GSM Phase 2+ Release 1999.

## Radio Interface Requirements

## Impact on UTRAN Functions

# IP Multicast Service (GPRS)

This chapter contains the requirements derived from GPRS specifications of IP Multicast service and the analysis regarding the UMTS radio interface Uu.

Note: 
The specification of the IP-Multicast service is part of the work item “GPRS – Point-To-Multipoint Services” of GSM Phase 2+ Release 1999.

## Radio Interface Requirements

## Impact on UTRAN Functions

# Multimedia Distribution Service (UMTS)

This chapter contains the requirements derived from UMTS Technical Specifications and the analysis regarding the radio interface Uu.

(Editor’s Note:
RAN WG2 has sent a Liaison statement to SA WG1 and WG2 requesting stage 1 and stage 2 specification of UMTS multicast services and describing the relation to SMS services. A reply is expected. Information is needed about the questions: In which annual release the UMTS Multicast services will be part? What are the requirements for the UMTS system and the protocols?)

## Radio Interface Requirements

## Impact on UTRAN Functions

# Annex A: Functions related to MDS (ffs.)

Previous WG2 Input documents:

R2-99075 (LGIC), R2-99076 (LGIC), R2-99218 (LGIC), R2-99219 (LGIC)

Input documents not presented yet:

R2-99077 (LGIC)

Related WG2 Output documents:

R2-99189 (TSG RAN WG2) LS to SA WG1 and SA WG2 on Multicast

(Editor’s note: The following text is taken from R2-99075 and should give a first overview of functions which should be analysed for MDS. Already made decisions are incorporated.)

Functions which should be analysed are listed below:

RRC functions:

Variable Rate Support

Dynamic Code usage

Dynamic Scheduling

QoS Support (e.g. repetition time)

(LGIC, R2-99075, for information)

RLC functions:

Unacknowledged multicast data transfer

Multicast Delivery

(LGIC, R2-99075, for information)

MAC functions:

Support fo multiple CTCH

Mapping and multiplexing/demultiplexing between CTCH and transport channels

Scheduling among CTCH

Support of dynamic rate change using TFCS

(LGIC, R2-99075, for information)

New types of transport channels are not required.

L1 functions:

Transmission of messages containing multicast data to specific groups of UEs. This service includes provision of the location function necessary to deliver mulitcast messages to a mobile, which is in idle or slotted mode.

DTX (discontinious transmission)

DRX (discontinious reception)

Support of multicast data transmission with multi-code

(LGIC, R2-99075, for information)

History

| Document history |
| --- |
| Date | Version | Comment |
| May 1999 | 0.0.1 | Skeleton without scope |
| June 1999 | 0.0.2 | Inclusion of scope and document structure as agreed at TSG RAN WG2 meeting #4, Berlin, 25-28 May 1999, distributed for e-mail approval |
| June 1999 | 0.1.0 | RAN WG 2 approved version with editoral changes and addition of subchapter x.2 (Impact on UTRAN Functions), x service specific chapters 6 to 10 |
| Rapporteur for TR 25.925 is: |
| Peter Krischan Mannesmann Mobilfunk GmbH Tel. : +49 211 533 2835 Fax : +49 211 533 2834 Email : peter.krischan@d2privat.de |
| This document is written in Microsoft Word 97. |