| 3GPP TSG-T2#4 / ETSI SMG4 Miami, US, 14-16 June 1999 | TSGT2#4(99)536 |
| --- | --- |
| CHANGE REQUEST No : |  | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
| Technical Specification GSM / UMTS: | 03.40 | Version: | 7.1.0 |  |
| Submitted to SMG | #29 | for approval | x | without presentation ("non-strategic") |  |  |
| list SMG plenary meeting no. here ­ | for information |  | with presentation ("strategic") |  |  |
| PT SMG CR cover form. Filename: crf26_3a.doc |

| Proposed change affects: | SIM |  | ME | x | Network |  |
| --- | --- | --- | --- | --- | --- | --- |

(at least one should be marked with an X)

| Work item: | SMS general improvements |
| --- | --- |

| Source: | T2-SWG3 | Date: | 15/6//1999 |
| --- | --- | --- | --- |

| Subject: | Clarification concerning SMSC address checking in the MS for concatenated messages and replace message types |
| --- | --- |

| Category: | F Correction |  | Release: | Phase 2 |  |
| --- | --- | --- | --- | --- | --- |
|  | A Corresponds to a correction in an earlier release |  |  | Release 96 |  |
| (one category | B Addition of feature |  |  | Release 97 |  |
| and one release | C Functional modification of feature | X |  | Release 98 | x |
| only shall be | D Editorial modification |  |  | Release 99 |  |
| marked with an X) |  |  |  |  |

| Reason for change: | In a network which comprises multiple SMSC’s it is possible for the MS to erroneously process a received SM if part of a concatenated message or a Replace Message type is delivered to the MS via different SMSC’s |
| --- | --- |

| Clauses affected: | 9.2.3.9 and 9.2.3.24.1and 9.2.3.24.8 |
| --- | --- |

| Other specs | Other releases of same spec |  | ® List of CRs: |  |
| --- | --- | --- | --- | --- |
| affected: | Other core specifications |  | ® List of CRs: |  |
|  | MS test specifications / TBRs |  | ® List of CRs: | 11.10 |
|  | BSS test specifications |  | ® List of CRs: |  |
|  | O&M specifications |  | ® List of CRs: |  |

| Other comments: | An LS has been sent from T2SWG3 to SMG7 requesting them to make an associated change to 11.10. |
| --- | --- |

<--------- double-click here for help and instructions on how to create a CR.

#### 9.2.3.9	TP-Protocol-Identifier (TP-PID)

The TP-Protocol-Identifier parameter serves the purposes indicated in subclause 3.2.3. It consists of one octet, and the bits in the octet are used as follows:

The MS will interpret reserved or unsupported values as the value 00000000 but shall store them exactly as received.

The SC may reject messages with a TP-Protocol-Identifier containing a reserved value or one which is not supported.

bits		usage

7   6
0   0		Assigns bits 0..5 as defined below
0   1		Assigns bits 0..5 as defined below
1   0		reserved
1   1		Assigns bits 0-5 for SC specific use

In the case where bit 7 = 0 and bit 6 = 0,

bit 5	indicates telematic interworking: 	
value = 0  :  no interworking, but SME-to-SME protocol	
value = 1  :  telematic interworking

In the case of telematic interworking, the following five bit patterns in bits 4..0 are used to indicate different types of telematic devices:

4..   .0

00000		implicit - device type is specific to this SC, or can be concluded on the basis of the address

00001		telex (or teletex reduced to telex format)

00010		group 3 telefax

00011		group 4 telefax

00100		voice telephone (i.e. conversion to speech)

00101		ERMES (European Radio Messaging System)

00110		National Paging system (known to the SC)

00111		Videotex (T.100/T.101)

01000		teletex, carrier unspecified

01001		teletex, in PSPDN

01010		teletex, in CSPDN

01011		teletex, in analog PSTN

01100		teletex, in digital ISDN

01101		UCI (Universal Computer Interface, ETSI DE/PS 3 01-3)

01110..01111		(reserved, 2 combinations)

10000		a message handling facility (known to the SC)

10001		any public X.400-based message handling system

10010		Internet Electronic Mail

10011..10111		(reserved, 5 combinations)

11000..11110		values specific to each SC, usage based on mutual agreement between the SME and the SC 	(7 combinations available for each SC)

11111		A GSM mobile station. The SC converts the SM from the received 	TP-Data-Coding-Scheme to any data coding scheme supported by that MS (e.g. the default).

If bit 5 has value 1 in an SMS-SUBMIT PDU, it indicates that the SME is a telematic device of a type which is indicated in bits 4..0, and requests the SC to convert the SM into a form suited for that device type. If the destination network is ISDN, the SC must also select the proper service indicators for connecting to a device of that type.

If bit 5 has value 1 in an SMS-DELIVER PDU, it indicates that the SME is a telematic device of a type which is indicated in bits 4..0.

If bit 5 has value 0 in an SMS-DELIVER PDU, the value in bits 4..0 identifies the SM-AL protocol being used between the SME and the MS.

Note that for the straightforward case of simple MS-to-SC short message transfer the Protocol Identifier is set to the value 0.

In the case where bit 7 = 0, bit 6 = 1, bits 5..0 are used as defined below

5 ..  . .0

000000		Short Message Type 0

000001		Replace Short Message Type 1

000010		Replace Short Message Type 2

000011		Replace Short Message Type 3

000100		Replace Short Message Type 4

000101		Replace Short Message Type 5

000110		Replace Short Message Type 6

000111		Replace Short Message Type 7

001000..011110		Reserved

011111		Return Call Message

100000..111100		Reserved

111101		ME Data download

111110		ME De-personalization Short Message

111111		SIM Data download

A short message type 0 indicates that the ME must acknowledge receipt of the short message but may discard its contents.

The Replace Short Message feature is optional for the ME and the SIM but if implemented it shall be performed as described here.

For MT short messages, on receipt of a short message from the SC, the MS shall check to see if the associated Protocol Identifier contains a Replace Short Message Type code.

If such a code is present, then the MS will check the  originating address and replace any existing stored message having the same Protocol Identifier code and originating address with the new short message and other parameter values. If there is no message to be replaced, the MS shall store the message in the normal way.The MS may also check the SC address as well as the Originating Address, However, in a network which has multiple SC’s, it is possible for a Replace Message type for an SM to be sent via different SC’s and so it is recommended that the SC address should not be checked by the MS unless the application specifically requires such a check.

If a Replace Short Message Type code is not present then the MS will store the message in the normal way.

# In MO short messages the SC reacts similarly but only the address of the originating MS or any other source is checked.

##### 9.2.3.24.1	Concatenated Short Messages

This facility allows short messages to be concatenated to form a longer message.

In the case of uncompressed 8-bit data, the maximum length of the short message within the TP-UD field is 134 (140-6) octets.

In the case of uncompressed GSM Default 7 bit data, the maximum length of the short message within the TP-UD field is 153 (160-7) characters.

In the case of 16 bit uncompressed USC2 data, the maximum length of the short message within the TP-UD field is 67 ((140-6)/2) characters. A UCS2 character must not be split in the middle; if the length of the User Data Header is odd, the maximum length of the whole TP-UD field is 139 octets.

In the case of compressed GSM Default alphabet 7 bit data, 8 bit data or UCS2 the maximum length of the compressed short message within the TP-UD field is 134 ( 140-6) octets including the Compression Header and Compression Footer, both or either of which may be present ( See subclause 3.9).

The maximum length of an uncompressed concatenated short message is 39015 (255*153) default alphabet characters, 34170 (255*134) octets or 17085 (255*67) UCS2 characters.

The maximum length of a compressed concatenated message is 34170 (255*134) octets including the Compression Header and Compression Footer ( see subclause 3.9 and Fig 9.2.3.24.1(a) below.

Figure 9.2.3.24.1.(a) Concatenation of a Compressed short message

The Information-Element-Data field contains information set by the application in the SMS-SUBMIT so that the receiving entity is able to re-assemble the short messages in the correct order. Each concatenated short message contains a reference number which together with the originating address and Service Centre address allows the receiving entity to discriminate between concatenated short messages sent from different originating SMEs and/or SCs. In a network which has multiple SC’s, it is possible for different segments of a concatenated SM to be sent via different SC’s and so it is recommended that the SC address should not be checked by the MS unless the application specifically requires such a check.

The TP elements in the SMS-SUBMIT PDU, apart from TP-MR, TP-SRR, TP-UDL and TP-UD, should remain unchanged for each SM which forms part of a concatenated SM, otherwise this may lead to irrational behaviour. TP-MR must be incremented for every segment of  a concatenated message as defined in subclause 9.2.3.6. A SC willl handle segments of a concatenated message like any other short message. The relation between segments of a concatenated message is made only at the originator, where the message is segmented, and at the recipient, where the message is reassembled. SMS-COMMANDs identify messages by TP-MR and therefore apply to only one segment of a concatenated message. It is up to the originating SME to issue SMS-COMMANDs for all the required segments of a concatenated message.

##### 9.2.3.24.8	Concatenated short messages, 16-bit reference number

This facility is an enhanced variant of the Concatenated Short Message facility (see subclause 9.2.3.24.1). The enhancement is a 16-bit reference number, instead of the short 8-bit reference number.  The larger reference number reduces the probability that two different concatenated messages are mistakenly sent with identical reference numbers to a receiver. Except for the size of the reference number this facility is identical to the Concatenated Short Message facility (see subclause 9.2.3.24.1).

In the case of uncompressed 8-bit data, the maximum length of the short message within the TP-UD field is 133 (140-7) octets.

In the case of uncompressed GSM Default 7 bit data, the maximum length of the short message within the TP-UD field is 151 (160-9) characters.

In the case of 16 bit uncompressed USC2 data, the maximum length of the short message within the TP-UD field is 66 ((140-7)/2) characters. A UCS2 character must not be split in the middle; if the length of the User Data Header is odd, the maximum length of the whole TP-UD field is 139 octets.

In the case of compressed GSM Default alphabet 7 bit data, 8 bit data or UCS2 the maximum length of the compressed short message within the TP-UD field is 133 ( 140-7) octets including the Compression Header and Compression Footer, both or either of which may be present ( see subclause 3.9).

The relation between compression and concatenation  is the same as for Concatenated Short Messages (see subclause 9.2.3.24.1).

The Information-Element-Data field contains information set by the application in the SMS-SUBMIT so that the receiving entity is able to re-assemble the short messages in the correct order. Each concatenated short message contains a reference number which together with the originating address and Service Centre address allows the receiving entity to discriminate between concatenated short messages sent from different originating SMEs and/or SCs. . In a network which has multiple SC’s, it is possible for different segments of a concatenated SM to be sent via different SC’s and so it is recommended that the SC address should not be checked by the MS unless the application specifically requires such a check.

The TP elements in the SMS-SUBMIT PDU, apart from TP-MR, TP-UDL and TP-UD, should remain unchanged for each SM which forms part of a concatenated SM, otherwise this may lead to irrational behaviour. TP-MR must be incremented for every segment of a concatenated message as defined in subclause 9.2.3.6. A SC will handle segments of concatenated message like any other short message. The relation between segments of a concatenated message is made at the originator, where the message is segmented, and at the receipient, where the message is reassembled. SMS-COMMANDs identify messages by TP-MR and therefore apply to only one segment of a concatenated message. It is up to the originating SME to issue SMS-COMMANDs for all the required segments of a concatenated message.