| 3GPP TSG-2 meeting #4 | Document | T2-99567 |
| --- | --- | --- |
| Miami, USA, 14-16 June 1999 |  |  |
| 3G CHANGE REQUEST |  |
|  | 27007 | CR |  | Current Version: |  |  |
| For submision to TSG |  | for approval | X |  |
|  | for information |  |  |
| Form: 3G CR cover sheet, version 1.0 The latest version of this form is available from: ftp://ftp.3gpp.org/Information/3GCRF-xx.rtf |
| Proposed change affects: | USIM |  | ME | X | UTRAN |  | Core Network |  |
| (at least one should be marked with an X) |
| Source: | Ericsson | Date: | 1999-05-26 |
| Subject: | ECSD asymmetry |
| 3G Work item: | EDGE circuit switched data |
| Category: | F Correction |  |  |  |  |
|  | A Corresponds to a correction in a 2G specification |  |  |  |  |
| (only one category | B Addition of feature |  |  |  |  |
| shall be marked | C Functional modification of feature |  |  |  |  |
| with an X) | D Editorial modification |  |  |  |  |
| Reason for change: | The introduction of user indicated asymmetry preference for non-transparent ECSD is in this CR proposed controlled by a new AT command, +CHSA |
| Clauses affected: | 6.18 (new) |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other 2G core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: |  |

<--------- double-click here for help and instructions on how to create a CR.

## 6.18	HSCSD non-transparent asymmetry configuration +CHSA

Table 1: +CHSA parameter command syntax

| Command | Possible response(s) |
| --- | --- |
| +CHSA=<mode> |  |
| +CHSA? | +CHSA: <mode> |
| +CHSA=? | +CHSA: (list of supported <mode>s) |

Description

Set command controls the preferred asymmetry bias for  non-transparent ECSD calls. Downlink biased asymmetry means that 8-PSK modulation is preferred downlink and GMSK modulation uplink.  Uplink based asymmetry means that 8-PSK modulation is preferred uplink and GMSK downlink.  The allowed preferred asymmetry bias may be MS Type dependant (see GSM 0x.xx). Changing of <mode> affects the current call only if <topRx> (refer +CHSN) was non-zero when call was established.

Test command returns values supported by the ME/TA as compound values.  The <mode> subparameter range indirectly indicates the MS Type; range (0-1) indicates MS Type A and range (0-2) indicates MS Type B.

NOTE:	ECSD is also controlled by +CHSD, +CHSN and +CHST.

Defined values

<mode>:

0	No preference

1	Downlink biased asymmetry

2	Uplink biased asymmetry

Implementation

Mandatory when non-transparent ECSD is implemented.