3GPP TSG T WG2, SWG1 (MExE)	Tdoc T2-99648

Helsinki, Findland

6 – 10 September, 1999

| CHANGE REQUEST No : |
| --- |
| Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
| Technical Specification GSM / UMTS: | 23.057 | Version | 1.3.0 |
|  | Submitted to SMG |
| for approval | X | without presentation ("non-strategic") |
| list plenary meeting or STC here ( | for information |
| with presentation ("strategic") | x |
|  | PT SMG CR cover form. Filename: crf26_3.doc |

| Proposed change affects: | SIM |
| --- | --- |
| ME | x | Network |

(at least one should be marked with an X)

Work item:

| Source: | Alcatel Business System | Date: | 23/08/99 |
| --- | --- | --- | --- |

| Subject: | Addition of actions in security domains and actions table |
| --- | --- |

| Category: | F Correction | x | Release: | Phase 2 |
| --- | --- | --- | --- | --- |
| A Corresponds to a correction in an earlier release |
|  | Release 96 |
|  | (one category | B Addition of feature |
|  | Release 97 |
|  | and one release | C Functional modification of feature |
|  | Release 98 |
|  | only shall be | D Editorial modification |
|  | Release 99 | x |
| marked with an X) |
| UMTS |

Reason for change:

Action access to trusted application is limited to action listed in security table. So we need to add several action access

Input / Output User interface

User notification

Date/clock

Serial port

Printer

Smart card

External application

GSM and other security function

| Clauses affected: | 8.2 |
| --- | --- |

| Other specs | Other releases of same spec |
| --- | --- |
| ( List of CRs: | Release 98 |
| affected: | Other core specifications |
| ( List of CRs: |
| MS test specifications / TBRs |
| ( List of CRs: |
| BSS test specifications |
| ( List of CRs: |
| O&M specifications |
| ( List of CRs: |

Other comments:

A melody is a user notification as a vibrator activation, a light flash.

Melody selection is a user preference, so it is cover by user preference category.

User notification associated to an event is a user preference.

WAP is providing a library to sign a content.

Java allow to launch an other application, WAP would like create a library to launch an application (SIM tool kit …)

SIM smart card access (send APU) is forbidden for all application what ever the application supported by SIM card (for example WIM application)

<--------- double-click here for help and instructions on how to create a CR.

Table 3: Security domains and actions

|  | MExE Security Domains |
| --- | --- |
| Actions |
| Operator | Manufacturer | Third Party |

User private data access 1

Read

Write

Get properties

Delete

Get Location Information

Read stored SMS

Delete stored SMS

Yes 2

Network access

Initiate a voice/data connection 3

Accept a voice/data connection 3

Call forward 4

Multiparty call 4

Call deflection 4

Explicit call transfer 4

Terminate an existing connection

Hold an existing connection

Resume an existing connection

Send point-point message (e.g. SMS, USSD) 4

Generate DTMF

Query network status

Get signal level

| Get call list | Yes | Yes 6 |
| --- | --- | --- |

Lifecycle management

Install a MExE Executable

Uninstall a MExE executable

Yes

Miscellaneous functions

| Get manufacturer software version | Yes |
| --- | --- |

Certificate management

Install a certificate for a given domain

Uninstall a certificate for a given domain

| Replace a certificate for a given domain | Yes 5 |
| --- | --- |
| GSM Security function | No |

Security function other than GSM

Data encryption

Verify a signature

Compute a digital signature

Hash a content

| Non repudiation | Yes |
| --- | --- |

Input output User interface

Input device (keyboard, mouse …)

| Output device (display, printer ?) | Yes10 |
| --- | --- |

User notification (text, image, sound, light, vibrator …)

Start / Stop notification

Get notification status

| Get available notifications | Yes |
| --- | --- |

Audio access

Sound generation to speaker (e.g. via stream)

Select Melody

Set speaker volume

| Get melody list | Yes |
| --- | --- |

Power management

Monitor the power state

| Change the power state | Yes |
| --- | --- |

Network selection/operator data access

Get IMSI

Get home network

| Select network | Yes | No |
| --- | --- | --- |

Device core function access

Start/stop radio

Turn on/off device

Read/write time and date

|  | No |
| --- | --- |
| Printer access | Yes |

External port access

Serial port (RS232, Irda, Bluetooth, USB …)

| Parallel port | No |
| --- | --- |
| SIM smart card access | No |

Smart card other than SIM card access

Send APDU

| Slot management (power on/off, ATR, reset, lock …) | Yes |
| --- | --- |

Application access

Get application list

Launch an application

Stop, suspend, resume an application

Yes8

Yes8

Yes9

User profile management

Activate a user profile

| Modify a user profile | No |
| --- | --- |

User preference management

Modify user preferences

Yes7

Legend for above footnotes:-

1 – User private data includes user files, phonebook, etc located on the MS.

2 – The user shall be able to specify data access permissions within the capabilities of the device.

3 – A network connection may be via any supported bearer service

4 – Multiparty, deflection, and explicit call transfer shall be permitted only to numbers explicitly supplied by the user to the MExE Executable. Modification of call forward numbers stored in the network shall only be permitted to numbers explicitly supplied by the user to the operator.

5 – Only the organisation whose public key is certified (or the organisation that certified the public key) can add, delete or replace a particular certificate.

6– The Third Party domain's permission to access the networking action depends on the provisioning mechanism as described in section 8.15

7 – Trusted applications only have permission to modify user preferences, and not to activate or de-activate them.  The user shall be able to specify for each domain, the preferences that applications in that domain can access.  All other preferences shall not be accessible to that domain. The default shall be that there is no access.  Single action user permission is the only type of user permission that shall be possible for changes to User Preferences.

8 – Device native application access is limited to manufacturer domain. 
SIM tool kit application access is limited to operator domain.
MExE application access is limited to the same issuer of application which want to use the action

9 – Access is limited to MExE application which launch the application (The user shall have a way to stop the application, himselft)

10 – Access request no user permission.