| 3GPP TSG-T2 #5 / ETSI SMG4 Helsinki, FINLAND, 6-9 September 1999 | TSGT2#5(99)671 |
| --- | --- |
| 3G CHANGE REQUEST | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
|  | 27.007 | CR |  | Current Version: | 3.1.0 |  |
| 3G specification number ( |  | ( CR number as allocated by 3G support team |
| For submision to TSG | #5 | for approval | x | (only one box should |
| list TSG meeting no. here ( | for information |  | be marked with an X) |
| Form: 3G CR cover sheet, version 1.0 The latest version of this form is available from: ftp://ftp.3gpp.org/Information/3GCRF-xx.rtf |
| Proposed change affects: | USIM |  | ME | x | UTRAN |  | Core Network |  |
| (at least one should be marked with an X) |
| Source: | SMG4 | Date: | 08/09/99 |
| Subject: | Phonebook storage |
| 3G Work item: | Technical Enhancements |
| Category: | F Correction |  |  |  |  |
|  | A Corresponds to a correction in a 2G specification |  |  |  |  |
| (only one category | B Addition of feature | x |  |  |  |
| shall be marked | C Functional modification of feature |  |  |  |  |
| with an X) | D Editorial modification |  |  |  |  |
| Reason for change: | To make it easier to choose a PIN2-locked phone book memory storage by sending the PIN2 as an optional parameter. |
| Clauses affected: | 8.11 |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other 2G core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: |  |

<--------- double-click here for help and instructions on how to create a CR.

8.11	Select phonebook memory storage +CPBS

Table 1: +CPBS parameter command syntax

| Command | Possible response(s) |
| --- | --- |
| +CPBS=<storage> [,<password>] | +CME ERROR: <err> |
| +CPBS? | +CPBS: <storage>[,<used>,<total>] +CME ERROR: <err> |
| +CPBS=? | +CPBS: (list of supported <storage>s) |

Description

Set command selects phonebook memory storage <storage>, which is used by other phonebook commands. If setting fails in an ME error, +CME ERROR: <err> is returned. Refer subclause 9.2 for <err> values.

Read command returns currently selected memory, and when supported by manufacturer, number of used locations and total number of locations in the memory.

Test command returns supported storages as compound value.

Defined values

<storage> values reserved by this ETS:

"DC"	ME dialled calls list (+CPBW may not be applicable for this storage) $(AT R97)$

"EN"	SIM (or ME) emergency number (+CPBW is not be applicable for this storage) $(AT R97)$

"FD"	SIM fixdialling-phonebook

"LD"	SIM last-dialling-phonebook

"MC"	ME missed (unanswered received) calls list (+CPBW may not be applicable for this storage)

"ME"	ME phonebook

"MT"	combined ME and SIM phonebook

"ON"	SIM (or ME) own numbers (MSISDNs) list (reading of this storage may be available through +CNUM also) $(AT R97)$

"RC"	ME received calls list (+CPBW may not be applicable for this storage) $(AT R97)$

"SM"	SIM phonebook

"TA"	TA phonebook

<password>: string type value representing the PIN2-code required when selecting PIN2-code locked <storage>s above, e.g. “FD”.

<used>: integer type value indicating the number of used locations in selected memory

<total>: integer type value indicating the total number of locations in selected memory

Implementation

Mandatory when phonebook read, find or write command, or direct dialling (refer subclause "Direct dialling from phonebooks") is implemented.