Liaison statement

To:	TSG CN1, TSG CN2, TSG T2

Cc:

From:	3GPP TSG S2

# Title:	Multimedia Call Control for UMTS R 99

TSG S2 would like to inform that TSG S2 has specified the following:

- H.323 shall be the multimedia call control protocol for the PS domain in UMTS R99.

Thus the revised principles for the support of multimedia in UMTS are (from 23.121):

P1) GSM/UMTS shall enable the provisioning of multimedia services and multivendor interworking between UE and network.

P2) Basic voice and PDP-context establishment shall be based on GSM CC/SM respectively.

P3) Handover and roaming to and from GSM shall be supported provided GSM is capable of supporting the ongoing media service.

P4) Ideas, concepts and procedures developed by other fora e.g. other standards bodies such as ITU, IETF etc. shall be included or referenced in GSM/UMTS when found suitable.

P5) To ensure multi-vendor inter-working and UE roaming, a single standardised multimedia protocol for CS domain and a single standardised multimedia protocol for PS domain shall be  selected for GSM / UMTS R99. This does not preclude the selection of other protocols by UMTS in the future.

- H.323 shall be the multimedia call control model for the PS domain in UMTS R99.

P6) For multimedia services the standardized multimedia protocol shall be run transparently via a PDP-context or a circuit-switched connection established using GSM SM/CC . This allows transparent hand-over and roaming between GSM and UMTS provided that GSM supports the QoS requirements.