| 3GPP TSG-T2 #6 Kyongju, KOREA, 4-6 October 1999 | TSGT2#6(99)822 |
| --- | --- |
| CHANGE REQUEST | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
|  | 27.007 | CR |  | Current Version: | 3.1.0 |  |
| GSM (AA.BB) or 3G (AA.BBB) specification number ( |  | ( CR number as allocated by MCC support team |
| For submision to: | T#5 | for approval | X |  | strategic |  | (for SMG |
| list approval meeting # here ( | for information |  |  | non-strategic |  | use only) |
| Form: CR cover sheet, version 1.1 for 3GPP and SMG The latest version of this form is available from: ftp://ftp.3gpp.org/Information/3GCRF-11.rtf |
| Proposed change affects: | (U)SIM |  | ME | X | UTRAN |  | Core Network |  |
| (at least one should be marked with an X) |
| Source: | Vodafone | Date: | 18/9/1999 |
| Subject: | AT command - Request GPRS service 'D' |
| Work item: | GPRS |
| Category: | F Correction |  | Release: | Phase 2 |  |
|  | A Corresponds to a correction in an earlier release | X |  | Release 96 |  |
| (only one category | B Addition of feature |  |  | Release 97 |  |
| shall be marked | C Functional modification of feature |  |  | Release 98 |  |
| with an X) | D Editorial modification |  |  | Release 99 | X |
|  |  |  | (releases phase2, 96, 97 and 98 apply only to GSM specifications) |
| Reason for change: | Editorial clarification and correction to 27.007 release ’99 for the ‘D’ modem compatibility command. This change was requested by implementers and clarifies the use of the ATD command for GPRS. |
| Clauses affected: | 10.2.1.1 |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other GSM core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: |  |

<--------- double-click here for help and instructions on how to create a CR.

#### 10.2.1.1	Request GPRS service 'D'

Table 1: D command syntax

| Command | Possible Response(s) |
| --- | --- |
| D*<GPRS_SC>[*[<called_address>] [*[<L2P>][*[<cid>]]]]# | CONNECT ERROR |

Description

This command causes the MT to perform whatever actions are necessary to establish communication between the TE and the external PDN.

The V.25ter 'D' (Dial) command causes the MT to enter the V.25ter online data state and, with the TE, to start the specified layer 2 protocol. The MT shall return CONNECT to confirm acceptance of the command prior to entering the V.25ter online data state. No further commands may follow on the AT command line.

The detailed behaviour after the online data state has been entered is dependent on the PDP type. It is described briefly in clauses 8 (for X.25) and 9 (for IP) of GSM 07.60. GPRS attachment and PDP context activation procedures may take place prior to or during the PDP startup if they have not already been performed using the +CGATT and +CGACT commands.

When the layer 2 protocol has terminated, either as a result of an orderly shut down of the PDP or an error, the MT shall enter V.25ter command state and return the NO CARRIER final result code.

If <called address> is supported and provided, the MT shall automatically set up a virtual call to the specified address after the PDP context has been activated.

If <L2P> and <cid> are supported, their usage shall be the same as in the +CGDATA command. The +CGDCONT, +CGQREQ, etc. commands may be used in the modem initialisation AT command string to set values for for PDP type, APN, QoS etc..

If <L2P> is not supported or is supported but omitted, the MT shall use a layer 2 protocol appropriate to the PDP type.

If <cid> is not supported or is supported but omitted, the MT shall attempt to activate the context using:

(a) any information provided by the TE during the PDP startup procedure, e.g. the TE may provide a PDP type and/or PDP address to the MT,

or, (b) a priori knowledge, e.g. the MT may implement only one PDP type,

or, (c) using the 'Empty PDP type' (GSM 04.08). (No PDP address or APN shall be sent in this case and only one PDP context subscription record shall be present in the HLR for this subscriber.)

This command may be used in both normal and modem compatibility modes.

NOTE.	The dial string conforms to the syntax specified in GSM 02.30.

Defined Values

<GPRS_SC>: (GPRS Service Code) a digit string (value 99) which identifies a request to use the GPRS

<called_address>: a string that identifies the called party in the address space applicable to the PDP. For communications software that does not support arbitrary characters in the dial string, a numeric equivalent may be used. Also, the character comma ',' may be used as a substitute for the character period '.'.
For PDP type OSP:IHOSS, the following syntax may be used for <called_address>:
	[<host>][@[<port>][@[<protocol>]]]
where <host>, <port> and <protocol> are defined in the +CGDCONT description. For communications software that does not support arbitrary characters in the dial string, a numeric equivalent to the hostname may be used. However, this should be avoided if at all possible.

<L2P>: a string which indicates the layer 2 protocol to be used (see +CGDATA command). For communications software that does not support arbitrary characters in the dial string, the following numeric equivalents shall be used:
0		NULL
1		PPP
2		PAD
3		X25
9yyyy		M-xxxx
Other values are reserved and will result in an ERROR response

<cid>: a digit string which specifies a particular PDP context definition (see +CGDCONT command).

Implementation

Optional if the +CGDATA command is supported. If the D command is provided, then support for <called_address>, <L2P> and <cid> are optional. If they are not supported but values are provided by the TE, the values shall be ignored and this shall not constitute an error.