| 3GPP TSG-T WG2 meeting #6 | Document | T2-99824 |
| --- | --- | --- |
| Kyongju, Korea, 4-6 October 1999 |  |  |
| 3G CHANGE REQUEST | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
|  | TS 07.07 | CR |  | Current Version: | 7.3.0 |  |
| 3G specification number ( |  | ( CR number as allocated by 3G support team |
| For submision to TSG | T2 | for approval | x | (only one box should |
| list TSG meeting no. here ( | for information |  | be marked with an X) |
| Form: 3G CR cover sheet, version 1.0 The latest version of this form is available from: ftp://ftp.3gpp.org/Information/3GCRF-xx.rtf |
| Proposed change affects: | USIM |  | ME | x | UTRAN |  | Core Network |  |
| (at least one should be marked with an X) |
| Source: | CN3 | Date: | 9909xx |
| Subject: | GPRS ATD command syntax |
| 3G Work item: |  |
| Category: | F Correction | x |  |  |  |
|  | A Corresponds to a correction in a 2G specification |  |  |  |  |
| (only one category | B Addition of feature |  |  |  |  |
| shall be marked | C Functional modification of feature |  |  |  |  |
| with an X) | D Editorial modification |  |  |  |  |
| Reason for change: | It can be foreseen that PDP type ‘IP’ will be more frequently used than PDP type ‘X25’. It would therefore be beneficial to the end-user if the order of the ‘parameters’ in the dialling string for the ATD command was changed, so that the ‘cid’ is the first parameter in the string. With the current definition the dialling string will look like ‘*99***<cid>#’, the proposed change will make it look like ‘*99*<cid>#’. |
| Clauses affected: | 10.2.1.1 |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other 2G core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: |  |

<--------- double-click here for help and instructions on how to create a CR.

#### 10.2.1.1	Request GPRS service 'D'

# Table 2: D command syntax

| Command | Possible Response(s) |
| --- | --- |
| D*<GPRS_SC>[*[<cid>] [*[<L2P>][*[<called_address>]]]]# | CONNECT ERROR |

# Description

The V.25ter 'D' (Dial) command causes the MT to enter the V.25ter online data state and, with the TE, to start the specified layer 2 protocol. The MT shall return CONNECT to confirm acceptance of the command prior to entering the V.25ter online data state. No further commands may follow on the AT command line.

When the layer 2 protocol has terminated, either as a result of an orderly shut down of the PDP or an error, the MT shall enter V.25ter command state and return the NO CARRIER final result code.

If <L2P> and <cid> are supported, their usage shall be the same as in the +CGDCONT command. The +CGDCONT command may be used in the modem initialisation AT command string to set values for for PDP type, APN, QoS etc..

This command may be used in both normal and modem compatibility modes.

NOTE.	The dial string conforms to the syntax specified in GSM 02.30.

# Defined Values

<GPRS_SC>: (GPRS Service Code) a digit string (value 99) which identifies a request to use the GPRS

<called_address>: a string that identifies thecalled party in the address space applicable to the PDP. For communications software that does not support arbitrary characters in the dial string, a numeric equivalent may be used. Also, the character comma ',' may be used as a substitute for the character period '.'.
For PDP type OSP:IHOSS, the following syntax may be used for <called_address>:
	[<host>][@[<port>][@[<protocol>]]]
where <host>, <port> and <protocol> are defined in the +CGDCONT description. For communications software that does not support arbitrary characters in the dial string, a numeric equivalent to the hostname may be used. However, this should be avoided if at all possible.

<L2P>: a string which indicates the layer 2 protocol to be used (see +CGDATA command). For communications software that does not support arbitrary characters in the dial string, the following numeric equivalents shall be used:
0		NULL
1		PPP
2		PAD
3		X25
9yyyy		M-xxxx
Other values are reserved and will result in an ERROR response

<cid>: a digit string which specifies a particular PDP context definition (see +CGDCONT command).

# Implementation

Optional if the +CGDATA command is supported. If the D command is provided, then support for <called_address>, <L2P> and <cid> are optional. If they are not supported but values are provided by the TE, the values shall be ignored and this shall not constitute an error.