| 3GPP TSG-T2 #6 / ETSI SMG4 Kyongju, KOREA, 4-6 October 1999 | TSGT2#6(99)902 |
| --- | --- |
| CHANGE REQUEST | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
|  | 23.040 | CR |  | Current Version: | V3.1.0 |  |
| GSM (AA.BB) or 3G (AA.BBB) specification number ( |  | ( CR number as allocated by MCC support team |
| For submision to: | T#5 | for approval | x |  | strategic |  | (for SMG |
| list approval meeting # here ( | for information |  |  | non-strategic |  | use only) |
| Form: CR cover sheet, version 1.1 for 3GPP and SMG The latest version of this form is available from: ftp://ftp.3gpp.org/Information/CRF-11.rtf |
| Proposed change affects: | (U)SIM |  | ME | x | UTRAN |  | Core Network | x |
| (at least one should be marked with an X) |
| Source: | T2 | Date: | 990928 |
| Subject: | New TP-PID value for delivery of ANSI-136 Short Messages |
| Work item: | Short Message Service (SMS) |
| Category: | F Correction |  | Release: | Phase 2 |  |
|  | A Corresponds to a correction in an earlier release |  |  | Release 96 |  |
| (only one category | B Addition of feature | x |  | Release 97 |  |
| shall be marked | C Functional modification of feature |  |  | Release 98 |  |
| with an X) | D Editorial modification |  |  | Release 99 | x |
|  |  |  | (releases phase2, 96, 97 and 98 apply only to GSM specifications) |
| Reason for change: | A new TP-PID value is required for the delivery of ANSI-136 teleservices using GSM SMS procedures. The opportunity has been taken to remove an ambiguity in a similar section. |
| Clauses affected: |  |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other GSM core specifications | x | ( List of CRs: | 11.14 |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: | This CR is part of GPRS-136HS project of UWCC |

<--------- double-click here for help and instructions on how to create a CR.

#### 9.2.3.9	TP-Protocol-Identifier (TP-PID)

The TP-Protocol-Identifier parameter serves the purposes indicated in subclause 3.2.3. It consists of one octet, and the bits in the octet are used as follows:

The MS will interpret reserved or unsupported values as the value 00000000 but shall store them exactly as received.

The SC may reject messages with a TP-Protocol-Identifier containing a reserved value or one which is not supported.

bits		usage

7   6
0   0		Assigns bits 0..5 as defined below
0   1		Assigns bits 0..5 as defined below
1   0		reserved
1   1		Assigns bits 0-5 for SC specific use

In the case where bit 7 = 0 and bit 6 = 0,

bit 5	indicates telematic interworking: 	
value = 0  :  no interworking, but SME-to-SME protocol	
value = 1  :  telematic interworking

In the case of telematic interworking, the following five bit patterns in bits 4..0 are used to indicate different types of telematic devices:

4..   .0

00000		implicit - device type is specific to this SC, or can be concluded on the basis of the address

00001		telex (or teletex reduced to telex format)

00010		group 3 telefax

00011		group 4 telefax

00100		voice telephone (i.e. conversion to speech)

00101		ERMES (European Radio Messaging System)

00110		National Paging system (known to the SC)

00111		Videotex (T.100/T.101)

01000		teletex, carrier unspecified

01001		teletex, in PSPDN

01010		teletex, in CSPDN

01011		teletex, in analog PSTN

01100		teletex, in digital ISDN

01101		UCI (Universal Computer Interface, ETSI DE/PS 3 01-3)

01110..01111		(reserved, 2 combinations)

10000		a message handling facility (known to the SC)

10001		any public X.400-based message handling system

10010		Internet Electronic Mail

10011..10111		(reserved, 5 combinations)

11000..11110		values specific to each SC, usage based on mutual agreement between the SME and the SC 	(7 combinations available for each SC)

11111		A GSM mobile station. The SC converts the SM from the received 	TP-Data-Coding-Scheme to any data coding scheme supported by that MS (e.g. the default).

If bit 5 has value 1 in an SMS-SUBMIT PDU, it indicates that the SME is a telematic device of a type which is indicated in bits 4..0, and requests the SC to convert the SM into a form suited for that device type. If the destination network is ISDN, the SC must also select the proper service indicators for connecting to a device of that type.

If bit 5 has value 1 in an SMS-DELIVER PDU, it indicates that the SME is a telematic device of a type which is indicated in bits 4..0.

If bit 5 has value 0 in an SMS-DELIVER PDU, the value in bits 4..0 identifies the SM-AL protocol being used between the SME and the MS.

Note that for the straightforward case of simple MS-to-SC short message transfer the Protocol Identifier is set to the value 0.

In the case where bit 7 = 0, bit 6 = 1, bits 5..0 are used as defined below

5 ..  . .0

000000		Short Message Type 0

000001		Replace Short Message Type 1

000010		Replace Short Message Type 2

000011		Replace Short Message Type 3

000100		Replace Short Message Type 4

000101		Replace Short Message Type 5

000110		Replace Short Message Type 6

000111		Replace Short Message Type 7

001000..011110		Reserved

011111		Return Call Message

100000..111011		Reserved

111100		ANSI-136 R-DATA

111101		ME Data download

111110		ME De-personalization Short Message

111111		SIM Data download

A short message type 0 indicates that the ME must acknowledge receipt of the short message but may discard its contents.

The Replace Short Message feature is optional for the ME and the SIM but if implemented it shall be performed as described here.

For MT short messages, on receipt of a short message from the SC, the MS shall check to see if the associated Protocol Identifier contains a Replace Short Message Type code.

If such a code is present, then the MS will check the originating address and replace any existing stored message having the same Protocol Identifier code and originating address with the new short message and other parameter values. If there is no message to be replaced, the MS shall store the message in the normal way. The MS may also check the SC address as well as the Originating Address. However, in a network which has multiple SCs, it is possible for a Replace Message type for a SM to be sent via different SCs and so it is recommended that the SC address should not be checked by the MS unless the application specifically requires such a check.

If a Replace Short Message Type code is not present then the MS will store the message in the normal way.

In MO short messages the SC reacts similarly but only the address of the originating MS or any other source is checked.

A Return Call Message indicates to the MS to inform the user that a call (e.g. a telephone call) can be established to the address specified within the TP-OA. The RP-OA contains the address of the SC as usual. The message content (if present) gives displayable information (e.g. the number of waiting voice messages). The message is handled in the same way as all other messages of the Replace Short Message Types.

The ME De-personalization Short Message is a ME-specific message which instructs the ME to de-personalities the ME (see GSM 02.22 [25]). The TP-DCS shall be set to Uncompressed, Default Alphabet, and Message Class 1 (ME-specific), which corresponds to a bit coding of 00010001.  The TP-UD field contains de-personalization information coded according to GSM 02.22 [25]. This information shall not be displayed by an ME which supports the scheme. The acknowledgement to this message is a SMS-DELIVER-REPORT for RP-ACK in which the TP-User-Data shall be coded according to GSM 02.22.

SIM Data download is a facility whereby the ME must pass the short message in its entirety including all SMS elements contained in the SMS deliver to the SIM using the mechanism described in GSM 11.11. The DCS shall be set to 8 bit message class 2 (either bit coding 1111 0110 or 00010110). The entire user data field is available for SIM Data download. If the DCS is not set to 8-bit message class 2 then the message shall be handled in the normal way by the ME.

ME Data download is a facility whereby the ME shall process the short message in its entirety including all SMS elements contained in the SMS deliver to the ME. The DCS shall be set to message class 1. The entire user data field is available for ME data download.

ANSI-136 R-DATA is a facility whereby the ME must pass the short message in its entirety, including all elements contained in the SMS DELIVER, to the SIM using the mechanism described in GSM 11.14. The DCS shall be set to 8-bit message class 2 (either bit coding 11110110 or 00010110).  If the DCS is not set to 8-bit message class 2 then the message shall be handled in the normal way by the ME.