| 3GPP/SMG Meeting #7 | Document | T2-991025 |
| --- | --- | --- |
| Ystad, Sweden, 22-26 November, 1999 |  | e.g. for 3GPP use the format TP-99xxx or for SMG, use the format P-99-xxx |
| CHANGE REQUEST | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
|  | 23.057 | CR |  | Current Version: | 1.5.0 |  |
| GSM (AA.BB) or 3G (AA.BBB) specification number ( |  | ( CR number as allocated by MCC support team |
| For submission to: |  | for approval | X |  | strategic |  | (for SMG |
| list expected approval meeting # here ( | for information |  |  | non-strategic |  | use only) |
| Form: CR cover sheet, version 2 for 3GPP and SMG The latest version of this form is available from: ftp://ftp.3gpp.org/Information/CR-Form-v2.doc |
| Proposed change affects: | (U)SIM |  | ME | X | UTRAN / Radio |  | Core Network |  |
| (at least one should be marked with an X) |
| Source: | Vodafone | Date: | 22-11-99 |
| Subject: | Clarification of the giving of user permission |
| Work item: | T2 SWG1 (MExE) |
| Category: | F Correction |  | Release: | Phase 2 |  |
|  | A Corresponds to a correction in an earlier release |  |  | Release 96 |  |
| (only one category | B Addition of feature |  |  | Release 97 |  |
| shall be marked | C Functional modification of feature | X |  | Release 98 |  |
| with an X) | D Editorial modification |  |  | Release 99 | X |
|  |  |  |  | Release 00 |  |
| Reason for change: | Some clarification of the giving of user permission is required. Further, a requirement that the user be warned if permission is being given to an untrusted application. “alias name” needs to be defined The forbidding of granting session permission to applets should be discussed. |
| Clauses affected: | 8.3 |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other GSM core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: |  |

<--------- double-click here for help and instructions on how to create a CR.

## 8.3		User permission types

The term “user permission” is defined to mean that the user can give permission for a specific action in one of the ways defined in Table 4. Support of blanket permission and single action permission is mandatory, but support of session permission is optional.

All prompts for user permission as described in table 4 must display the a user friendly name identifying the signer of the corresponding MExE executable, if available.  The user shall be able to request to see the “subject” field of the certificate of the signer (“subject” here refers to the “subject” fields of WTLS and X.509 certificates and an equivalent field for any other format of certificate).  If an application, for which user permission is being sought, is untrusted, the fact that the application is untrusted shall be visually indicated to the user whenever user permission is sought.The user shall be prompted for user permission relating to all action groups listed in the table 3 that are required by the MExE executable. If a prompt for permission relates to more than one action, e.g. networking and user data, then it shall list the individual action group permissions which will be granted, though the action group permissions can all be granted with a single user action. This condition applies to any prompts relating to user permissions in table 4.

Note that blanket permission cannot be used for uninstalled MExE executables e.g. applets, WMLS.