| 3GPP TSG-T3 (USIM) #11 | Document | T3-99431 |
| --- | --- | --- |
| Sophia-Antipolis, 8 – 10 December 1999 |  | e.g. for 3GPP use the format TP-99xxx or for SMG, use the format P-99-xxx |
| CHANGE REQUEST | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
|  | 3G 21.111 | CR |  | Current Version: | V 3.0.0 |  |
| GSM (AA.BB) or 3G (AA.BBB) specification number ( |  | ( CR number as allocated by MCC support team |
| For submision to: | TSG-T | for approval | x |  | strategic |  | (for SMG |
| list approval meeting # here ( | for information |  |  | non-strategic |  | use only) |
| Form: CR cover sheet, version 1.1 for 3GPP and SMG The latest version of this form is available from: ftp://ftp.3gpp.org/Information/CRF-11.rtf |
| Proposed change affects: | (U)SIM | x | ME | X | UTRAN / radio |  | Core Network |  |
| (at least one should be marked with an X) |
| Source: | Gemplus | Date: | 09.12.1999 |
| Subject: | Clarification of USIM application selection |
| Work item: |  |
| Category: | F Correction |  | Release: | Phase 2 |  |
|  | A Corresponds to a correction in an earlier release |  |  | Release 96 |  |
| (only one category | B Addition of feature |  |  | Release 97 |  |
| shall be marked | C Functional modification of feature | X |  | Release 98 |  |
| with an X) | D Editorial modification |  |  | Release 99 | x |
|  |  |  | (releases phase2, 96, 97 and 98 apply only to GSM specifications) |
| Reason for change: | It should be clearly stated that the user shall be able to choose which application to select between all available applications in the UICC, for instance between 2 USIM applications. |
| Clauses affected: | 6.1 |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other GSM core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: |  |

<--------- double-click here for help and instructions on how to create a CR.

# 6	Logical issues

## 6.1	Application selection

In a multiapplication environment, a flexible application selection method is required. The application identifier defined in ISO/IEC 7816-5 [5] and EG 201 220 [6] should be used for application selection. Direct application selection and the EFDIR concept of ISO/IEC 7816-4 [4] shall be followed.

A mechanism for the ME and the UICC shall be specified in order to allow the user :
-	to know which selectable applications are present on the UICC, 
-	to select and activate one amongst those which are available and supported by the ME

This will permit him for instance to choose between 2 different USIM applications.

## 6.2	Simultaneous access

A mechanism shall be specified for simultaneous access to several files or applications.

# 7	Service Requirements

## 7.1	User profiles

Each USIM shall contain at least one user profile [FFS].

## 7.2	Data transfer

A mechanism allowing highly secure transfer of applications and/or associated data to/from the UICC/USIM shall be specified in line with the requirements in 3GPP 22.01 [2]. This requires a secure transfer mechanism. GSM 02.48 [20] and GSM 03.48 [21] could be considered here, however this is limited to the case where the application to be downloaded runs in the context of an existing subscription. The security requirements in the case where, for instance, a new USIM or other application has to be downloaded, requires further study.

It is envisaged that in early USIM specifications, the transfer of subscription-related applications (e.g. SIM application toolkit applications) will be specified. The generic application download (e.g. download of a new USIM) is not likely to be included in these early specifications.

Application creation comprises file creation and other administrative operations on the, as well as negotiation of code type or language.

## 7.3	Application execution environment

An application execution environment may exist on the UICC/USIM which includes the functionality defined in GSM 11.14 [9].

## 7.4	Profile exchange

A mechanism for the ME, the USIM and the network to exchange service capabilities shall be specified. The following exchange of service capabilities may occur:

## -	ME services capabilities may be provided to the USIM/UICC;