| 3GPP TSG-T3 (USIM) Meeting #15 | Document | T3-000405 |
| --- | --- | --- |
| San Diego, USA, 16-18 August 2000 |  | revised from T3-000378 |
| CHANGE REQUEST | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
|  | TS 31.102 | CR | 046 | Current Version: | V3.2.0 |  |
| GSM (AA.BB) or 3G (AA.BBB) specification number ( |  | ( CR number as allocated by MCC support team |
| For submission to: | TSG-T #9 | for approval | X |  | strategic |  | (for SMG |
| list expected approval meeting # here ( | for information |  |  | non-strategic |  | use only) |
| Form: CR cover sheet, version 2 for 3GPP and SMG The latest version of this form is available from: ftp://ftp.3gpp.org/Information/CR-Form-v2.doc |
| Proposed change affects: | (U)SIM | X | ME | X | UTRAN / Radio |  | Core Network |  |
| (at least one should be marked with an X) |
| Source: | T3 | Date: | 18/08/2000 |
| Subject: | Alignment of EF(CCP2) with EF(ECCP) |
| Work item: | T.E.I. |
| Category: | F Correction | X | Release: | Phase 2 |  |
|  | A Corresponds to a correction in an earlier release |  |  | Release 96 |  |
| (only one category | B Addition of feature |  |  | Release 97 |  |
| shall be marked | C Functional modification of feature |  |  | Release 98 |  |
| with an X) | D Editorial modification |  |  | Release 99 | X |
|  |  |  |  | Release 00 |  |
| Reason for change: | EF(CCP2) should have the same structure as EF(ECCP), as defined in GSM 11.11 R'99 |
| Clauses affected: | 4.2.38 |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other GSM core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: |  |

### 4.2.38	EFCCP2 (Capability Configuration Parameters 2)

This EF contains parameters of required network and bearer capabilities and terminal configurations associated with a call established using a fixed dialling number, an MSISDN, a service dialling number, an incoming call or an outgoing call. It is referred by EFFDN, EFMSISDN, EFSDN, EFICI and EFOCI at USIM ADF level.

| Identifier: '6F4F' | Structure: linear fixed | Optional |
| --- | --- | --- |
| SFI: '16' |  |
| Record length: X bytes, X(15 | Update activity: low |
| Access Conditions: READ PIN UPDATE PIN DEACTIVATE ADM ACTIVATE ADM |
| Bytes | Description | M/O | Length |
| 1 to X | Bearer capability information element | M | X bytes |

-	Bearer capability information elements.

-	Contents and Coding:

-	see 3G TS 24.008 [9]. The Information Element Identity (IEI) shall be excluded, i.e. the first byte of the EFCCP2 record shall be Length of the bearer capability contents.

- unused bytes are filled with 'FF'