TSG-Terminals Working Group 3 (USIM) meeting #4	TSGT3#4(99)113

Tokyo 19th - 21th April, 1999	Page  1

Source:	NTT DoCoMo and Japan Telecom

Title:	Proposed modifications of the UPDATE access condition for EFMSISDN

___________________________________________________________________________

- Introduction

This document describes modifications of the UPDATE access condition for EFMSISDN.

- Add the ADM level to the UPDATE access condition for EFMSISDN

The UPDATE access condition for EFMSISDN should be modified to ‘CHV1/ADM’ so that operator can choice which AC is to be applied. In PDC, Network operator writes MSISDN with subscription information. So user never change his/her own number (MSISDN) in ME.

- Proposed Content

Proposed contents are as follows.

Table 1. EFMSISDN structure

| Identifier: 'xxxx' | Structure: linear fixed | Optional |
| --- | --- | --- |
| Record length: X+14 bytes | Update activity: low |
| Access Conditions: READ CHV1 UPDATE CHV1/ADM (fixed during administrative management) INVALIDATE ADM REHABILITATE ADM |
| Bytes | Description | M/O | Length |
| 1 to X | Alpha Identifier | O | X bytes |
| X+1 | Length of BCD number/SSC contents | M | 1 byte |
| X+2 | TON and NPI | M | 1 byte |
| X+3 to X+12 | Dialling Number/SSC String | M | 10 bytes |
| X+13 | Capability/Configuration Identifier | M | 1 byte |
| X+14 | Extension1 Record Identifier | M | 1 byte |