| 3GPP TSG-T3 (USIM) Meeting #14 | Document | T3-000273 |
| --- | --- | --- |
| Visby, Sweden, 24-26 May 2000 |  | corresponds to 9-00-0237 |
| CHANGE REQUEST | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
|  | 31.102 | CR | 032 | Current Version: | V3.1.0 |  |
| GSM (AA.BB) or 3G (AA.BBB) specification number ( |  | ( CR number as allocated by MCC support team |
| For submission to: | TSG-T #8 | for approval | X |  | strategic |  | (for SMG |
| list expected approval meeting # here ( | for information |  |  | non-strategic |  | use only) |
| Form: CR cover sheet, version 2 for 3GPP and SMG The latest version of this form is available from: ftp://ftp.3gpp.org/Information/CR-Form-v2.doc |
| Proposed change affects: | (U)SIM | X | ME | X | UTRAN / Radio |  | Core Network |  |
| (at least one should be marked with an X) |
| Source: | T3 | Date: | 26/05/2000 |
| Subject: | New "length of HPLMN" field in EF(AD) |
| Work item: | T.E.I. |
| Category: | F Correction | X | Release: | Phase 2 |  |
|  | A Corresponds to a correction in an earlier release |  |  | Release 96 |  |
| (only one category | B Addition of feature |  |  | Release 97 |  |
| shall be marked | C Functional modification of feature |  |  | Release 98 |  |
| with an X) | D Editorial modification |  |  | Release 99 | X |
|  |  |  |  | Release 00 |  |
| Reason for change: | The ability to extract the right number of digits from the IMSI to determine the HPLMN (5 or 6 digits) |
| Clauses affected: | 4.2.18 |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other GSM core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: |  |

### 4.2.18	EFAD (Administrative data)

This EF contains information concerning the mode of operation according to the type of USIM, such as normal (to be used by PLMN subscribers for 3G operations), type approval (to allow specific use of the ME during type approval procedures of e.g. the radio equipment), cell testing (to allow testing of a cell before commercial use of this cell), manufacturer specific (to allow the ME manufacturer to perform specific proprietary auto-test in its ME during e.g. maintenance phases).

It also provides an indication of whether some ME features should be activated during normal operation.

It may as well provide information about the length of the HPLMN, which is part of the International Mobile Subscriber Identity (IMSI).

| Identifier: '6FAD' | Structure: transparent | Mandatory |
| --- | --- | --- |
| File size: 4+X bytes | Update activity: low |
| Access Conditions: READ ALW UPDATE ADM INVALIDATE ADM REHABILITATE ADM |
| Bytes | Description | M/O | Length |
| 1 | UE operation mode | M | 1 byte |
| 2 – 3 | Additional information | M | 2 bytes |
| 4 | length of HPLMN in the IMSI | O | 1 byte |
| 5 - 4+X | RFU | O | X bytes |

-	UE operation mode

Contents: mode of operation for the UE

Coding:

Initial value

- normal operation										'00'

- type approval operations									'80'

- normal operation + specific facilities							'01'

- type approval operations + specific facilities						'81'

- maintenance (off line)									'02'

- cell test operation										'04'

-	Additional information

Coding:

- specific facilities (if b1=1 in byte 1);

Byte 2 (first byte of additional information):

|  |  | b8 | b7 | b6 | b5 | b4 | b3 | b2 | b1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  |  |  | RFU (see 3G TS 31.101) |

Byte 3:

|  |  | b8 | b7 | b6 | b5 | b4 | b3 | b2 | b1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  |  |  | b1=0: OFM to be disabled by the ME b1=1: OFM to be activated by the ME |
|  |  |  |  |  |  |  |  |  |  | RFU (see 3G TS 31.101) |

The OFM bit is used to control the Ciphering Indicator as specified in GSM 02.07 [3]

- ME manufacturer specific information (if b2=1 in byte 1).

- length of HPLMN in the IMSI :

Contents:

The length indicator refers to the number of digits, used for extracting the HPLMN from the IMSI (e.g. 6 digits for PCS1900 for NA)

Coding:

Byte 4:

|  |  | b8 | b7 | b6 | b5 | b4 | b3 | b2 | b1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  |  |  | '0000' : no value is provided any other value : this value codes the number of digits of the HPLMN in the IMSI |
|  |  |  |  |  |  |  |  |  |  | RFU (see 3G TS 31.101) |