| 3GPP T3 ad hoc meeting #08 Munich, Germany, 26 - 27 July, 2000 | Tdoc T3z000067 |
| --- | --- |

Subject:

Source: Requirement proposal for STK browser/interpreter

The following document presents the Schlumberger proposal for a high level requirement list for the "STK browser/interpreter" considering the following objectives:

The STK browser/interpreter shall

-Support the mediation of a maximum of WML 1.1 services

-Support the running of STK-based services stored on a centralised server (including end-to-end secured services, location based services, dual slots,…)

-Be able to evolve to support PKI, and bearer independent protocol

Considering the above, the design criteria should be:

-minimize bandwidth requirement

-keep the interpreter/browser footprint under 24Ko

This requirement list has been derived from the requirement list proposed for the SIM @lliance Toolbox (S@T).

SUPPORT OF STK commands

| REF. NUMBER | DESCRIPTION | RANKING |
| --- | --- | --- |
| 100 | STK commands for WML Mediation Display Text, Get Inkey, Get Input, Select Item, Set Up Menu, The system should be able to welcome future STK commands WML script mediation is not required | Must Do Must Do Must Do Must Do Must Do Must Do Must Do |
| 110 | Additional STK commands to support current STK services Provide Local Information, Send SM, Send SS, Send USSD, Set Up Call (including send DTMF commands), Send DTMF Refresh Generic STK command Interface | Must Do Must Do Must Do Must Do Must Do Must Do Must Do Must Do |
| 120 | Additional STK commands to support multiple card services Power On card, Power Off card, Perform Card APDU, Get reader status, | Should do Should do Should do Should do |
| 130 | Remaining STK commands for 11.14 completion More Time, Play Tone, Poll Interval, Polling Set Up Event List , Event download Set Up idle mode text Timer Management Call control | Should do Should do Should do Should do Should do Should do Should do Should do |

Non STK FEATURES

| 200 | support WML mediation Go (branching to a URL) Variables (referencing, subtituting,…) SoftKey support (Do tags) Card and Deck navigation Navigation shortcuts (Go Home, Go Back, Exit, Help) | Must Do Must Do Must Do Must Do Must Do |
| --- | --- | --- |
| 210 | Processing commands to support existing STK services Variable test / Conditional branching Environment variables Concatenation of strings | Must Do Must Do Must Do |
| 220 | Ciphering Point-to-point security (Gateway to Browser): Encrypt/Decrypt/MAC with DES(56bit)/TDES(EDE CBC – 112bit) End-to-End security for parameters and variables Capability to evolve to PKI security | Must Do Must Do Must Do |
| 230 | Plug-In The browser execute an external function | Should Do |

System Requirement

| 300 | Session and Transaction protocol For connection robustness over the SMS bearer and future bearer independence. | Must Do |
| --- | --- | --- |
| 310 | Fetch browser/interpreter profile For optimisation of mediation per client characteristics For forward/backward compatibility | Must Do |
| 320 | Administration commands To administrate the browser (resident decks, environment variables) independently of its implementation | Must Do |
| 330 | Interpreter mode ("Local browsing") The interpreter shall be able to transparently interpret page stored locally or fetched from a server. | Must Do |
| 340 | Bookmark Bookmark by the end user of the current page. | Should Do |
| 350 | Support of SMS and UCS2 For page and variable manipulation. | Must Do |