| 3GPP T3 (USIM) ad hoc #10 / WAP forum ad hoc Winchester, UK, 5 - 6 September, 2000 | Tdoc T3z000118 |
| --- | --- |

WAP/SAT interaction

Source:	ALCATEL

Date:	04 September 2000

ALCATEL would like to raise some concerns regarding the “Modes of starting browser”. It seems to be difficult to implement correctly these modes due to several possible interpretations.

- Does the “Proxy/gateway ID data object” included in the LAUNCH BROWSER command, matches with the “Proxy Name” defined in the WAP specification. Could we ask T3 to clarify this ?

- When the command qualifier is set to 04, the notion of secured session is required, but it is necessary to study different cases.

- if no “Provisioning file reference” or  “Proxy/Gateway ID” data object are  provided in the proactive command, the Gateway used is unknown (we assume the browser will use the default one (defined by the user!)) and there is no way for the SIM to know if the secured session is allowed.

- if “Provisioning file reference” or  “Proxy/Gateway ID” data object are provided in the proactive command, the port to be used is then given in the configuration data and may be in contradiction with the command qualifier.

3.   What is the ME’s behaviour when a contradiction is found ?