## Slide 1: IPv6 in 3GPP Evolved Packet System I-D: draft-korhonen-v6ops-3gpp-eps
Nokia Siemens Networks
Nokia

## Slide 2: Some Common Terminology..
EPC = Evolved Packet Core
RAN = Radio Access Network
EPS = Evolved Packet System (EPC + RAN)
eNodeB = evolved NodeB i.e. base station in EPS
3GPP Access = radio system developed by 3GPP
Non-3GPP Access = radio system not developed by 3GPP
UE = User Equipment i.e., a mobile host, wireless device
APN = Access Point Name
PDN = Packet Data Network i.e. an IP network
SGSN = Serving GPRS Support Node
GGSN = Gateway GPRS Support Node
SGW = Service Gateway
PDN-GW = Packet Data Network Gateway
MME = Mobility Management Entity
Release-x = named version of the GPRS/EPS architecture (eg. Rel 4, Rel 5 etc)

## Slide 3: Basic Evolved Packet System Architecture
Architecture supports EUTRAN and legacy 2G/3G accesses as well
PtP link is established between the UE and the P-GW
User-plane traffic always tunneled over the transport network.
User-plane addressing independent of transport network addressing and IP versions.
PDN-GW
SGW
MME
eNodeB
UE
S1-MME
S11
S1-U
S5/S8
LTE-Uu
Dual-Stack EPS Bearer
PDN / IP Services
SGi

## Slide 4: PDN Connection
A PDN Connection is an association between an UE and a PDN, represented by one IPv4 address and/or one /64 IPv6 prefix
A PDN is identified by an APN
Each PDN is accessed via a PDN-GW
A PDN is responsible for the IP address/prefix management for the UE.
On an UE a PDN Connection is equivalent (or visible to an IP stack) as a virtual network interface.
Pre-Release-8 “equivalent” for a PDN Connection is the PDP Context (used in GPRS).

## Slide 5: EPS Bearer Model
A logical concept of a bearer has been defined as an aggregate of one or more IP flows related to one or more services.
The EPS bearer is between the UE and the PDN-GW, and used to transport IP (v4 and/or v6) packets
The UE performs the binding of the UL IP flows and the PDN-GW performs the binding of the DL IP flows

## Slide 6: Access Point Name concept
UEs and network use APNs to identify a network (e.g. internet, corporate intra-network, etc) and to some extent the associated services in that network.
APNs are piggybacked on the administration of the DNS namespace.
During the connection (bearer) setup, APNs are used (by SGSN/MME) to discover the gateway (GGSN/PDN-GW) that provides the IP connectivity to the network identifier by the APN.

## Slide 7: Address Management
IPv4 Address Configuration.
  Two methods: DHCPv4 or within the EPS bearer setup signaling (the common way)
  DHCP is optional on both the UE and the P-GW
IPv6 Address Configuration.
  One method: Stateless Address Autoconfiguration after the bearer setup.
  A single /64 prefix is only supported

## Slide 8: EPS Bearer Types
IPv4 only bearer.
  The bearer is configured with one IPv4 address.
  The link is “IPv4 only”.
IPv6 only bearer.
  The bearer is configured with one /64 prefix.
  The link is “IPv6 only”.
IPv4v6 bearer.
  The bearer is configured with both IPv4 address and one /64 prefix.
  New bearer type since Release-8.
  The link is “dual-stack”.
  V4v6 bearer type is the default in Rel-8 and beyond
  Rel 9 has also introduced the DS PDP context type for UTRAN and EDGE

## Slide 9: PDN Connection Establishment
UE
eNodeB
MME
SGW
PDN-GE
HSS/AAA
Authentication and Authorization
RB Setup
1)
1)
2)
3)
3)
4)
5)
4)
6)
7)
8)
9)
10)
11)
12)
13)
UL Data
DL Data
Attach request
Auth/AuthZ phase
Create Session Request
Create Session Response
Initial context setup request/Attach accept
Radio bearer reconfig
Initial context setup response
Direct transfer
Attach complete
UE starts sending UL data
Modify bearer request
Modify bearer response
DL data transmission starts

## Slide 10: Dual-Stack Approach for IP Access
Networks prior to Release-8
  Dual-stack connectivity possible by opening two parallel PDP Contexts of types IPv4 and IPv6.
  Shows up as two separate interfaces to the IP stack.
Networks from Release-8 onwards.
  A single IPv4v6 PDN Connection in addition to having separate v4 and v6 PDN connections.
  Shows up as one interface with both IPv4 and IPv6 addresses to the IP stack (with v4v6 type).

## Slide 11: Dual-stack approach
eNodeB
S-GW
MME
P-GW
DS-PDN
Type v4v6 PDN connection
BS
SGSN
GGSN
IPv4-PDN
IPv4-APN
IPv4-PDP Context
GGSN
IPv6-APN
IPv6-PDN
IPv6-PDP Context

## Slide 12: A live example
The DS approach is demonstrated using a Nokia N900 device using the T-Mobile USA network
For details:
  http://people.nokia.net/~patil/Nokia/N900-IPv6/

## Slide 13: Demo setup
BS
SGSN
GGSN
IPv4-PDN
IPv4-APN
IPv4-PDP Context
IPv6-APN
IPv4v6-PDN
IPv6-PDP Context
T-Mobile USA commercial 3G network
Nokia N900
Ack: Cameron Byrne of TMO USA for supporting us in this demo
NAT64

## Slide 14
Attached via the T-Mobile 3G network with Ipv6 and IPv4 PDP contexts.

## Slide 15: Summary/Conclusion
3GPP networks support IPv4 and IPv6 connectivity in EPS and earlier architecture
Type v4v6 PDN connection is optimal for providing a UE with DS connectivity
Transition to IPv6 via the DS approach ensures that legacy devices and services do not suffer from service disruption and hence a pragmatic solution