## Slide 1
T-MOBILE USA View on LTE Carrier Aggregation with Unlicensed Spectrum
3GPP Workshop on “LTE-U”, Sophia Antipolis (France), June 13th 2014

## Slide 2: Our objectives for the RAN Study (1/2).
    Only licensed assisted LTE access to unlicensed spectrum to be considered.
    Global as well as national regulation situation should be analyzed.
    LTE-U technology benefits over other state of the art technologies (i.e. IEEE 802.11ac/ad) should be evaluated.
    Co-Existence with other technologies (i.e. WiFi) using the same spectrum should be studied.

## Slide 3: Our objectives for the RAN Study (2/2).
    Study of required changes to LTE-A to support unlicensed spectrum aggregation should be performed.
    Both LBT-not-required and LBT-required cases should be studied. Standardization completion timelines for both cases should be independent.
    the study should aim for a global harmonized solution taking into account regulation differences in different regions, including LBT, to foster a vibrant eco-system.
    Solutions should be competitive compared to other state of art technologies.

## Slide 4: Requirements for potential realisation (1/3).
    “Supplemental downlink” and “Carrier Aggregation” mode to be supported, both mandatory for terminals.
    “Co-location” and “non co-location” deployments should be possible.
    Indoor and Outdoor deployments to be supported (Focus on operator planned deployment).

## Slide 5: Requirements for potential realisation (2/3).
    A unified global solution must be developed.
    Complete 5.x GHz band (5150 – 5350, 5470 – 5725 and 5725 – 5875 MHz) to be supported and mandatory for terminals
        Potential other bands should be identified during the study phase

## Slide 6: Requirements for potential realisation (3/3).
    Any LTE band can be used as the PCC to carrier aggregate with SCC in the unlicensed band.
    Min. 80MHz bandwidth using unlicensed spectrum in addition to up to 5x 20 MHz CC in licensed spectrum.
    4x4 MIMO to be optionally supported.
<Any LTE band as PCC + LTE-U SCC>
4x 20MHz
+
min. 80MHz (4x 20MHz) unlicensed
UE
eNodeB
4x4
20
20
20
20
20
up to 5x 20MHz licensed
Band 1
Band 3
Band 7
Band 8
Band 20
…

## Slide 7: Supported Spectrum for Global Solution
100 MHz
100 MHz
255 MHz
100 MHz
100 MHz
255 MHz
100 MHz
100 MHz
100 MHz
255 MHz
100 MHz
100 MHz
100 MHz
100 MHz
180 MHz
150 MHz
125 MHz (operators only)
N / A
„Band A“
„Band B“
„Band C“
up to150MHz BWFA [ECC Rec. (06)04]
5150
5250
5350
5470
5755
5875
f (MHz)
5725
typ. 23 dBm EIRP
typ. >30 dBm EIRP
Preference for 5.8GHz Wi-Fi bands that do not have DFS and LTB requirements (band A, 5150-5250MHz and band D, 5725-5825MHz)

## Slide 8
Thank You
Notes: Justin