## Slide 1: Views on 5G: Key Radio Technologies and Standardization
Sep.17-18, 2015
Fujitsu Ltd.
RWS-150046
3GPP TSG RAN Workshop on 5G
Phoenix, Arizona, Sep.17-18, 2015

## Slide 2: Demanded Features for 5G Networks
Business expansion capability
  Create new values and business models based on 5G network
  IoT is one of the promising targets
  Should be an evolving system with timely incorporation of new service/use-case requirements
Improved user/application QoE
  Always sufficient quality of user experience (immersive experience)
  Always sufficient quality for various applications (IoT, V2X, etc.)
  Provision of consistent E2E QoE, Ubiquitous coverage
Higher scalability/adaptability and efficiency
  Efficient use of radio resource and energy
  Low cost (UE, CAPEX/OPEX)
  Flexibility to match the requirements of different use-cases
  Based on cloud-based virtualized network

## Slide 3: Timeline of IMT-2020
2015 | 2016 | 2017 | 2018 | 2019 | 2020
Rel.13
Rel.14
Rel.15
Rel.16
Channel model for >6GHz
Scenarios & requirements
Phase-2 WI
5G SI(s) (R14~R16)
Phase-1 (To be deployed in 2020)
  New RAT (up to 30GHz)
  eMBB
  Massive MTC, Ultra reliable MTC
  E2E latency reduction
  Flexible TDD
  Enhancements for UDN
LTE Evolution
  eMBB
      eLAA for 5GHz unlicensed
      Flexible duplex (FDD)
      WiGig aggregation
      MUST
  Latency reduction, V2X, …
LTE Evolution continues
ITU-R IMT-2020
Completion
Phase-2 (To be deployed in 2022~2023)
  Fulfil all the ITU-R IMT-2020 requirements
  Extension of BW using new spectrum above 6GHz (New RAT up to 100GHz, BF/MIMO)
  Support of full-duplex operation
  (mmWave) wireless back/fronthaul
Forward/
Backward
compatibility
Dec.2019
Technologies for LTE evolution can also be used also for 5G new RAT. So, the above classification may not be strictly followed.
Further evolution
WRC19
Phase-1 WI (R14, R15)
Sep.2018

## Slide 4: Candidate Features Targeting Phase 1
Extension of BW using existing spectrum (assigned by WRC15)
  New RAT for bands up to 30GHz
    Not required to be backwards compatible with LTE
  Multi-RAT combinations (e.g. CA, DC) with:
    LTE, LTE-A
    eLAA: DL+UL, additional frequency bands
    eLWI: WiFi /WiGig integration
Flexible TDD
  Adapt to diverse traffic in 5G era via universal TDD frame structure
Ultra Dense Network (UDN)
  UDN / Large-scale CoMP (Indoor/Outdoor)
    Measurement/feedback enhancements for interference control
New features
  E2E Latency reduction
    Connected mode: Short TTI, Optimization (PDCP) for TCP/HTTP, eLIPA/eSIPTO
    Idle mode: Fast idle-active transitions
  Support of massive numbers of MTC devices (mMTC)
  Ultra-reliable and critical communications (uMTC)
(e.g. 4400-4900MHz)

## Slide 5: Spectrum Extension Scenario for MBB
New RAT
LAA/
WLAN
WiGig
(for indoor)
eLWI
New RAT
(Def by WRC15
+ Current IMT bands)
WiGig
(for indoor)
CA/DC/LWI
eLWI
LTE
LAA(DL only)/
WLAN
CA/LWI
CA/DC
New RAT
Phase 2
CA/DC
CA/DC/LWI
CA/DC
Rel.13
5G Phase 1
5G Phase 2
f
f
f
CA/DC
LTE
CA/DC
LTE
CA/DC
MBB: Mobile broadband, CA: Carrier aggregation, DC: Dual connectivity, LWI: LTE-WLAN integration
(Def by WRC19)
Up to 20Gbps peak rate
OFDM-based with flexible numerology
1ms latency
* Standalone operation of 5G RAT should also be supported
5GHz
(Unlicensed)
60GHz
(Unlicensed)
5GHz
(Unlicensed)
60GHz
(Unlicensed)
5GHz
(Unlicensed)
(Def by WRC15
+ Current IMT bands)
LAA/
WLAN

## Slide 6: New RAT Design
t
Supporting various traffic requirements, considering available spectrum, channel conditions and device types
  eMBB, mMTC and uMTC
  Urban Macro, Urban Micro, Indoor Hotspot, etc.
Support dynamic/semi-static combination of new and existing spectrally efficient waveforms based on OFDM (e.g. FBMC) with flexible numerology
PHY/MAC parameters to be optimized for 100 MHz or higher carrier bandwidth (mainly for spectrum newly assigned by WRC15)
  Maximum achievable bit-rate likely to be limited by available spectrum
Forward compatible
  Design should not restrict introduction of new features envisaged for Phase 2

## Slide 7: Ultra Dense Network (UDN)
Fronthaul Network
Dynamic virtual cell configuration
Dense deployment of small cells improves bps/Hz/m2
  Increased inter-cell interference limits the area throughput
  Increased requirements (bandwidth, scalability, cost) for backhaul/fronthaul networks
Dynamic virtual cell configuration based on traffic distribution
  UE-centric virtual cell configuration via large scale cooperation among distributed small cells for interference control
  Excessive lean carrier design should be considered
Flexible backhaul/fronthaul network
  Reconfigurable MP-to-MP, Packet-based
    Architectural design and functional splitting
    Heterogeneous transmission links (Optical, wireless, DSL)
  Study RAN specification impacts
BBU/GW

## Slide 8: Candidate Features Targeting Phase 2
Stand alone operation for the New RAT
  If not included in Phase 1
Extension of BW using new spectrum
  New RAT features and optimizations for bands up to 100GHz (assigned in WRC19)
    Cost-effective use of mmWave radio channels
    DC, CA, Multi-RAT combinations
    Beamforming
    Massive MIMO
Evolution of duplex scheme
  Support of (quasi-)full-duplex operation
    Design of flexible TDD (Phase1) should take into account this feature for forward compatibility
    Coexistence of non-full-duplex and full-duplex operation

## Slide 9: Operation of New RAT above 6GHz
Channel susceptible to shadowing, large penetration loss
Beamforming gain and diversity to compensate the large path loss
  Potentially high device cost/complexity and power consumption
  Limited mobility and cell/beam discovery/tracking
Features for above 6GHz (up to 100GHz)
    ~2GHz BW
    Support of multiple radio interface parameters for future proofing and optimization for different scenarios (e.g. Indoor/outdoor, frequency bands, fronthaul/backhaul applications)
  Beam-space multiplexing of multiple TX signals
    Analog/digital hybrid beamforming
      Low power consumption & cost
      One analog beam serves multiple UEs
  Beam-space + site diversity to compensate shadowing
New RAT
New RAT+
f
LTE
(Def by WRC19)
Dual connectivity SCell (First priority)
Standalone operation should also be supported

## Slide 10: Evolution of Duplex Schemes
DL Layer
UL Layer
Space Division (Full) Duplex
In-band Full Duplex
5G Phase 1:
  Flexible TDD
Same frequency
≈2x duplexing gain
Multi-level self-interference cancellation (Antenna, RF, Digital) required
≤2x duplexing gain
Relaxed TP to RP interference suppression requirement due to the larger coupling loss b/w TP and RP
Tight coordination
Technologies
  TP/RP separation
  TP to RP interference suppression
  Flexible DL-UL ratio
LTE-A:
  Dynamic TDD (eIMTA)
5G Phase 2:
  Full Duplex
LTE-further evolution:
  Flexible Duplex (FDD)

## Slide 11: Summary
Phase 1 should focus on a new RAT for Sep.2018
  Flexible radio interface specification targeting:
    Frequency bands up to 30GHz
    Mobile Broadband
    Massive MTC
    Ultra-reliable MTC
    Ultra-Dense Networks
    Forwards compatibility to Phase 2 and beyond
  May meet a subset of 5G requirements
  Phase 2 has to meet all ITU-R IMT-2020 requirements by Dec.2019
  Extended frequency bands: 0.3GHz to100GHz
  Evolution of duplex scheme (inc. full-duplex)
  RAN work to support:
    Backhaul/Fronthaul evolution for Ultra-Dense Networks
    Core Network improvements

## Slide 12
Copyright 2010 FUJITSU LABORATORIES LIMITED
11