## Slide 1
[6GWS-250230]
Tejas Networks’ views on 6G Radio Network
6G Workshop,
Mar 10th-11th 2025, Incheon, South Korea
6GWS-250230

## Slide 2
Motivation for the next generation
wireless system

## Slide 3
The design considerations for 6G architecture fall mainly into:
  Evolutionary changes involving enhancing existing 5G features such as
    Immersive communication (Improved User and system throughput, Supporting higher mobility, Improved spectrum efficiency, High accuracy positioning)
    Massive Communication (Higher density deployment)
    Hyper Reliable low latency communication (reducing latency and reliable handover)
  6G specific features designed from ground-up to support new scenarios and requirements such as
    Ubiquitous connectivity (improving TN coverage, TN-NTN integration)
    ISAC (Sensing based application)
    AI and communication (Network for AI and AI for Network),
  6G includes other overarching aspects
    Sustainability (Energy efficiency)
    Security and privacy
Considerations for 6G architecture design

## Slide 4
Overview of Tejas Networks’ proposal for 6G

## Slide 5
Immersive Communication
Distributed Ultra Massive MIMO (UM-MIMO) / Extreme MIMO (X-MIMO): Improved Coverage, spectral efficiency, Capacity & Energy Efficiency
UM-MIMO for 6G FR1 & FR3 bands (with MRSS) and e-MIMO for FR2 (and sub THz bands?)
Studying RIS Integration for dense urban and sub-urban coverage
Massive Communication
Battery less devices as replacement of UHF RFID based devices
Hyper reliable low latency Communication
Supporting energy efficient communications with UAV
Dynamic SBFD, In-Band Full Duplex (IBFD) with partially overlapping band for reducing latency
CHO, LTM support in Day-1 for improved reliability in mobility
NTN enhancement for IoT
Considerations for evolutionary changes for 6G

## Slide 6
Ubiquitous Connectivity
Enhanced TN UL coverage through better waveform and higher MIMO
Seamless Integration: Terrestrial and satellite networks unite for uninterrupted global connectivity.
Multi-Access Connectivity: Integration of non-3GPP access methods broadens connectivity options and improves user experience.
AI and communication
Evolution AI for Network: Dynamic waveforms adapting to the environment, CSI compression/prediction, beam forming and Air interface level positioning
AI for network operations: Predictive network and network automation
Support for Network for AI: Federated learning, distributed computing of core/access/edge
ISAC
Network as Sensor: Communication infrastructure doubles as a sensing platform for 3D spatial awareness.
Enhanced Functionality: Precise object detection and localization.
Diverse Applications: interfaces for Object identification and velocity with AI enhanced applications
Study of RIS in sensing and Sub-THz sensing
Considerations for newer use case and scenarios

## Slide 7
Sustainability (Energy Efficiency)
Enhanced Power Control Mechanisms, Energy-Efficient Waveforms, RACH optimization etc. for improving energy efficiency
Introducing energy consumption related data collection for network optimization.
Security and Privacy
Study use of 256-bit or 512-bit encryption is good enough to make network quantum safe
SIB level security and MAC-CE level security
Improving trust levels for Network Function and AI model management
Considerations for overarching aspects

## Slide 8
Detailed proposals for 6G

## Slide 9
Motivation
In 5G, the data is transmitted with wideband MCS which is suboptimal.
The MCS being constant for all the layers results in lower spectral efficiency.
New measurements can help to utilize the native AI-ML capabilities.
Proposal
Enhanced air interface for 6G to study:
  Sub-band specific MCS should be supported by the air-interface.
  Layer specific modulation order and/or code-rate can exploit spatial domain diversity.
  New physical layer measurements such as position estimates and channel statistics.
Enhancements to the Air interface
Air interface for improving spectral efficiency
Impact: RAN
Notes: This slide alone is enhanced in child slide

## Slide 10
Proposal
Ultra-Massive MIMO at higher frequencies
Study channel model for new spectrum, to augment the applicability of UM-MIMO in the new bands, like 6-24 GHz and Sub-THz
Study for CSI-RS ports ( >128 ports)
Distributed Ultra-Massive MIMO
Study Distributed UM-MIMO for energy efficient networks with enhanced capacity and coverage
Ultra Massive MIMO/Extreme-MIMO
Motivation
UM-MIMO at higher frequencies
5GA CSI enhancements up to 128 ports are targeting FR1 spectrum
An increased number of CSI-RS ports benefits small form factor antenna arrays operating at higher carrier frequencies, when considered with optimized sounding and feedback compression mechanisms.
Distributed UM-MIMO
Distributed Massive MIMO enhances data rate for user devices at the cell edges.
Different multiple access techniques for distributed MIMO systems can provide higher throughput, massive connectivity, low latency, and high reliability with user fairness operating at higher frequencies
Reduces problems inherent with handover and inter-cell interference.
Enabling immersive communication
Primary Impact: RAN
Notes: This slide alone is enhanced in child slide

## Slide 11
Motivation
Release 19 of 5G is working on specifying Sub band full duplex which provides:
Increased uplink throughput up to 25%
Enhanced Uplink Coverage by allowing repetition across SBFD slots and non SBFD slots.
6G should aim at specifying in band full duplex as next step to:
Aids in sensing and jointly designing communication functions
Help in radio imaging.
Support low latency and high data rate to address immersive communication applications.
Proposal
RAN to study in band full duplex design to solve the following issues:
Self-interference handling both at UE and gNB​
CLI handling for Inter gNB and inter UE
Collision handling of Uplink and Downlink data.​
Multi TRP support with full duplex.​
Capability to handle legacy and Full Duplex UEs​
Supporting the feature in all bands supported in 6G
Duplex Evolution in 6G
Enabling immersive communication use case
Primary Impact: RAN
Notes: This slide alone is enhanced in child slide

## Slide 12
Motivation
5G-Adv Rel 19 A-IoT is restricted to indoor use cases
Existing battery less device technology such as UHF RFID technology has limitations - lack of interference management in dense deployment, shorter range (only indoor use case).
There is a need to support battery less devices (BLDs) as a better coverage replacement of UHF RFID in outdoor scenario
Proposal
Extend the application of battery-less device for outdoor applications such as vehicle tracking, outdoor sensor, etc.
Communication between BLDs and the NR base stations either directly or indirectly via an intermediate node.
Coexistence between the BLDs and legacy UEs.
Enhancing the QoS by communicating with the nearby devices using alternate frequencies through beam steering.
Unified signaling for LP-WUS and BLDs to optimize the OFDM resource utilization.
Battery-less IoT devices
Enabling Massive communication
Primary Impact: RAN, CT, SA
Notes: This slide alone is enhanced in child slide

## Slide 13
Motivation
UAV typically have limited onboard energy due to size and weight constraints so there is a need for energy-efficient communication
Proposal
Study on E2E system architecture for UAV
  Investigate joint UAV trajectory and RIS passive beamforming design to improve energy efficiency in 6G networks
RIS-Aided UAV Communication in 6G
Enabling HRLLC and ubiquitous communication
Primary Impact: RAN, SA
Notes: This slide alone is enhanced in child slide

## Slide 14
Motivation
  Specification efforts in 5G includes:
  5G NTN Integration:
  Rel. 17: NR-NTN & IoT-NTN for satellites (Doppler/GNSS compensation, RedCap).
  Rel. 18: Ka-band support, AI/ML positioning, hybrid TN/NTN mobility (SIB19).
  Rel. 19: Regenerative payloads, reduced GNSS dependency, on-demand SSB for energy savings.
  IoT Expansion:
  NB-IoT/eMTC over satellites for agriculture, logistics, and disaster recovery.
  Unaddressed Gaps
  NTN architectures "still evolving" with TN dependence.
  Static beam prediction; no real-time constellation optimization
  Device Constraints: Smartphone NTN limited to SOS/emergency use
  High-Speed Mobility: No handover solutions for NTN (>500 km/h).
Proposal
  Native Architecture:
  Study to Embed NTN support in 6G protocols (Doppler compensation, latency-aware scheduling).
  Unified Air Interface:
  Study OFDM-based TN/NTN harmonization for seamless handovers.
  Study split Architecture design aimed at supporting mobility, Carrier Aggregation between TN and NTN cells
  Study to improve throughput for Direct to Satellite Connectivity
6G Non-Terrestrial Networks
Enabling Ubiquitous Communication
Primary Impact: RAN, CT, SA
Notes: This slide alone is enhanced in child slide

## Slide 15
Motivation
IAB/WAB/NCR is still not a cost-effective option for coverage enhancement
Better coverage, overall 6G network power saving improvements possible with RIS
RIS consisting of a large array of controllable antenna elements can also be used for sensing/object detection.
Proposal
Study on RIS integration
  Study channel model and channel estimation for gNB-RIS-UE path (RAN1/RAN4).
  Study signaling interfaces between gNB-RIS and RIS-UE.
  Study use of RIS for sensing and object detection
  Study RIS aided energy efficiency by optimizing the number of active beams
Reconfigurable Intelligent Surfaces (RIS)
Enabling Ubiquitous Connectivity
Primary Impact: RAN
Notes: This slide alone is enhanced in child slide

## Slide 16
Motivation
Normative work for AI/ML was restricted to CSI compression and beam management for 5G
Potential improvement in CSI compression, Beam Management, Coding, Codebook, and Rate Matching in particular for FR3 (6-24 GHz)
Potential energy saving gains by reduction of actual measurement and using predicted measurement
Achievable positioning accuracy in 5G for outdoor scenario is limited to 3m due NLoS dominant links
Proposal
Study AI/ML-Driven Optimization for 6G in the following areas:
  CSI: Predict & compress feedback, reducing overhead.
  Beam Management: Real-time beam selection & tracking.
  Channel Coding: Neural network-based encoders/decoders for better error correction.
  Codebook: Dynamic updates based on real-time conditions.
  Resource Allocation: AI-optimized resource allocation.
Study the enhancement in positioning (cm level accuracy) based on AI-ML techniques.
AI/ML-Driven Optimization for Air interface
Enabling AI for Network design
Impact: RAN
Notes: This slide alone is enhanced in child slide

## Slide 17
Motivation
Motivation
Basic channel model study was done in 5G-Adv
ISAC is a key usage scenario enabled in 6G and is expected to help in indoor obstacle sensing, outdoor detection of UAV, identify railway and road crossing etc.
Proposal
Enhance ISAC architecture to support 6G use cases by
Model the RCS of various objects
Ensure the objects are detected with minimal false alarms
Incorporating AI/ML techniques to improve probability of detection as well as localization accuracy
In future, see option for sensing fusion with non-3GPP elements for improving sensing localization
Integrated Sensing and Communication
Enabling joint sensing and communication use case
Impact: RAN, CT, SA
Notes: This slide alone is enhanced in child slide

## Slide 18
Motivation
To utilize state of the art AI/ML based approaches for network optimization:
  Leverage cloud-native technologies to provide contextualized, on-demand network data
  Utilizing state-of-the art AI/ML techniques for optimization that result in increased spectrum efficiency, QoE, with reliability, security, trust and reduced energy consumption.
Aspects which needs to be tackled in 6G:
  HetNets with disparate data types
  Volume and velocity of data
  Zero / low-touch deployment
  Agile and adaptable to varying network topologies.
  Intent based / declarative workflows enabling quick, no-code use case definition
  Encourage EdgeAI
Proposal
  Unified data-ingestion and exposure framework:
  A single cloud-native workflow that works across all heterogeneous technologies with disparate data-types.
  Provides ability to introduce exogenous data for better contextual understanding (earthquake / special event notifications)
  Contextualize disparate data-types: A unified interface that provides data on-demand via API driven data-exposure function
  Intent driven agentic AI :
  Agentic AI that can be invoked by declarative policies or via GenAI-style chat-based client.
  Study on use of LLMs for
  Study on multi-agent ensembles for multi-objective optimization.
  Study on Federated and Distributed learning for model generalization, data privacy, reduction in footprint and latency.
AI enabled Network optimization
Enabling AI for Network design
Impact: RAN, CT, SA
Notes: This slide alone is enhanced in child slide

## Slide 19
Impact: RAN, SA
Motivation
Network energy savings was studied and specified in 5G in Release 18 and release 18:
  NES techniques were developed as an afterthought in later stage of 5G resulting in reduced support for large UE footprint (due to issues in supporting legacy UEs).
  Enhancement restricted to Low Load scenarios
Aspects which needs to be tackled in 6G:
  Medium and High Load Scenarios,
  Enhanced waveform efficiency,
  Improved resource allocation strategies
  Seamless network reconfiguration
  Exploitation of Spatial and Temporal Distribution of UE.
Proposal
  Enhanced Power Control Mechanisms: Study frameworks for fine-grained transmission power adjustments and power-efficient antenna configurations.
  Study Energy-Efficient Waveforms for:
    Optimized Modulation Schemes to balance spectral efficiency, out-of-band emissions, and power consumption.
    Dynamic Waveform adaptation (optimize based on network load conditions).
  RACH optimization: Study improved initial access methods for improved resource utilization.
  Paging and Cell Reselection Optimization: Adaptive Paging techniques that minimize unnecessary wake-up signaling and optimize cell reselection based on energy efficiency.
  Study on enhanced dynamic adaptation techniques for UE specific signals or channels for network energy saving.
  Study on Joint Energy saving between Network and UE
Network Energy Optimization
Enabling sustainability : Energy Optimality for 6G must be built Natively
Notes: This slide alone is enhanced in child slide

## Slide 20
Motivation
Lack of protection for System Information messages lead to Man-in-the-Middle (MITM) type of attack
MAC-CE is currently used for critical triggers such as LTM cell switch and lack of security at MAC-CE level is an open issue.
Security for SI and MAC-CE can be considered as baseline requirement in 6G
Existing security maximum key length (128 bits) might not be sufficient for a Post-Quantum world
Proposal
Study methods to protect broadcasted System information messages
Study security for MAC-CE messages
Study security for other unprotected Layer 2 messages such as RLC Status PDU, PDCP status PDU etc
Study use of 256bits or higher length keys for encryption and integrity protection will be sufficient security in a post quantum world.
Security related aspects for 6G
Enabling Security and Privacy in 6G
Impact: RAN, CT, SA
Notes: This slide alone is enhanced in child slide

## Slide 21
Motivation
5G provided multiple options to upgrade from 4G to 5G creating segmentation of market
Have a single option can help for focused effort in 3GPP
Proposal
Study for supporting Voice based on existing IMS mechanism (same interface as in 5GC)
Study to reuse UDM, PCF, NEF, NRF, NSSF, SCP, NSSAF, EASDF, NSACF, AUSF from 5G for 6G
Study to upgrade AMF, SMF, UPF to support 6G with backward integration to 5G
Study reusing existing IWF for non-3GPP and enhance N3IWF for supporting NTN.
Core related aspects of 6G
Enabling seamless migration from 5G
Impact: CT, SA
Notes: This slide alone is enhanced in child slide

## Slide 22
Motivation
5G provided an option to spectrum share with 4G based on DSS
6G should also provide spectrum sharing with respect to Multi-RAT spectrum sharing
Proposal
Study MRSS based spectrum sharing
Spectrum sharing aspects of 6G
Enabling seamless migration from 5G
Impact: RAN, CT, SA
Notes: This slide alone is enhanced in child slide

## Slide 23
JISHNU@TEJASNETWORKS.com